## Slide 1
COURSE SLIDES · WSQ
Cisco Certified Network Professional (CCNP) for ENCOR Training
WSQ Course Code: TGS-2024044052
Conducted by Tertiary Infotech Academy Pte Ltd · UEN 201200696W
Version v6.0 · 7 September 2026
© 2026 Tertiary Infotech Academy Pte Ltd. All rights reserved. · www.tertiarycourses.com.sg

## Slide 2
COURSE ADMINISTRATION
Welcome & Housekeeping
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
2

## Slide 3
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
1
Three times a day
Take the AM, PM and Assessment digital attendance — mandatory for every WSQ-funded course.
2
Trainer shows the QR
The trainer or administrator displays the digital attendance QR code from the SSG portal.
3
Scan and submit
Scan the QR code with your mobile phone camera and submit your attendance.
4
75% minimum
A minimum of 75% attendance is required to be eligible for assessment and funding.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
3

## Slide 4
YOUR TRAINER · GENERAL
About the Trainer
?
Your Trainer
General Trainer template — to be completed by the trainer
NAME
____________________________________________
TITLE / DESIGNATION
____________________________________________
QUALIFICATIONS
____________________________________________
AREAS OF EXPERTISE
____________________________________________
TRAINING & INDUSTRY EXPERIENCE
____________________________________________
CONTACT
____________________________________________
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
4

## Slide 5
YOUR TRAINER
About the Trainer
AA
Dr Alfred Ang
Principal Trainer Tertiary Infotech Academy Pte Ltd
ROLE
Principal Trainer, Tertiary Infotech Academy Pte Ltd
EXPERTISE
Enterprise networking, Cisco routing and switching, network security and network automation.
DELIVERS
WSQ courses on CCNA, CCNP Enterprise, network security and infrastructure automation.
FOUNDER
Founder and lead instructor at Tertiary Infotech / Tertiary Courses.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
5

## Slide 6
ICE-BREAKER
Let's Know Each Other
• Your name, organisation and role.
• Your networking experience — CCNA, hands-on with Cisco IOS, or new to enterprise networking.
• The network you look after today: campus, branch, data centre or wireless.
• What you want to be able to configure or troubleshoot by Friday.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
6

## Slide 7
HOUSEKEEPING
Ground Rules
1
Set your mobile phone to silent mode.
2
Participate actively — no question is too small.
3
Mutual respect: agree to disagree.
4
One conversation at a time.
5
Be punctual; return from breaks on time.
6
75% attendance is required.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
7

## Slide 8
COURSE PORTAL
Login to LMS and Download Course Material
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
8
Log in at lms-tms.tertiaryinfotech.com with your registered email and the OTP sent to your inbox, then open this course to download the slides and Learner Guide.

## Slide 9
LMS / TMS · lms-tms.tertiaryinfotech.com
Download Your Course Material
1
1 · Go to the LMS portal
Open https://lms-tms.tertiaryinfotech.com in your browser.
2
2 · Log in
Sign in with the account e-mail you used to register for this course.
3
3 · Open this course
Select 'Cisco Certified Network Professional (CCNP) for ENCOR Training'.
4
4 · Download
Download the Trainer Slides, Learner Guide and Lesson Plan (PDF).
5
5 · Get the labs
Open the labs folder link on the course page for every Packet Tracer topology.
6
6 · Keep them open
You may use these materials during the open-book assessment.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
9

## Slide 10
LMS / TMS · STEP BY STEP
How to Download Your Course Material
1
Open the LMS
lms-tms.tertiaryinfotech.com
2
Log in
Your registration e-mail
3
Find this course
CCNP ENCOR · TGS-2024044052
4
Open Courseware
Slides · LG · LP · Labs
5
Download the PDFs
Keep them for the open book
BEFORE WE START
Download all four documents now — the assessment is open book, but only these approved materials are permitted.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
10

## Slide 11
SKILLS FRAMEWORK · TSC
Skills Framework Alignment
1
TSC Title
Network Configuration
2
TSC Code
ICT-DIT-3009-1.1
3
K1 / A1
Key network components and their interdependencies; translating organisational to technical requirements.
4
K2 / A2
Techniques for implementing and configuring servers, devices and network components.
5
K3 / A3
Features of network management tools; implementing devices per the network blueprint.
6
K4 / A6
Configuration of network servers and devices; procedures for reporting and stability assessment.
7
K5 / A4
Network access management; managing user network access to organisational guidelines.
8
K6 / A5
Network tracking and assessment tools; identifying suitable network management tools.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
11

## Slide 12
WHAT YOU'LL ACHIEVE
Learning Outcomes
1
LO1 · Translate requirements
Translate organizational networking needs into technical configurations by selecting appropriate network components, considering their functions and interdependencies.
2
LO2 · Select components
Identify and choose key network components for configuration, utilizing techniques in server and device implementation aligned with technical requirements.
3
LO3 · Implement devices
Implement a variety of servers and devices effectively, following the organizational network blueprint to enhance network performance and reliability.
4
LO4 · Manage access
Manage network access, ensuring compliance with organizational guidelines and specifications to maintain secure and efficient user connectivity.
5
LO5 · Deploy tools
Select and deploy network management tools effectively, optimizing network performance and user experience in line with organizational needs.
6
LO6 · Report and assess
Conduct regular network reporting and administration, employing assessment tools to ensure network stability and alignment with organizational objectives.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
12

## Slide 13
SIX TOPICS · 35 HANDS-ON LABS
Course Outline — The Six ENCOR Exam Domains
1
Topic 01 — Enterprise Architecture · 15%
Design principles · wireless design · SD-WAN · SD-Access · QoS · switching mechanisms
2
Topic 02 — Virtualization Technologies · 10%
Hypervisors · virtual machines · virtual switching · VRF · GRE and IPsec · LISP and VXLAN
3
Topic 03 — Network Infrastructure · 30%
Layer 2 · Layer 3 routing · wireless · IP services — the largest exam domain
4
Topic 04 — Network Assurance · 10%
Diagnostics · NetFlow · SPAN/RSPAN/ERSPAN · IP SLA · DNA Center · NETCONF and RESTCONF
5
Topic 05 — Network Security · 20%
Device access control · AAA · ACLs and CoPP · REST API security · wireless security · security design
6
Topic 06 — Network Automation · 15%
Python · JSON · YANG · DNA Center and vManage APIs · REST responses · EEM · orchestration tools
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
13

## Slide 14
ENCOR 350-401 · BLUEPRINT WEIGHTING
Where Course Time Goes — Exam Domain Weighting
Chart: 
| 01 Enterprise Architecture | 02 Virtualization Technologies | 03 Network Infrastructure | 04 Network Assurance | 05 Network Security | 06 Network Automation
Share of the ENCOR exam (%) | 15 | 10 | 30 | 10 | 20 | 15
WHAT THE DATA SHOWS
Infrastructure carries 30% of the exam — nearly a third — and Security another 20%. Half the exam sits in these two domains, so half your revision time belongs there. Days 3 and 4 are built around that.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
14

## Slide 15
SCHEDULE · 40 INSTRUCTIONAL HOURS
Lesson Plan — 5 Days, 8 hours/day
Days 1–3
Days 4–5
• Day 1 — Enterprise Architecture — design, switching paths, campus LAN and high availability
– Digital Attendance (AM) · Introductions · Learning Outcomes
– Topic 1 Enterprise Architecture (Labs 1–5)
• Day 2 — Virtualization Technologies — hypervisors, VRF, GRE/IPsec, LISP and VXLAN
– Topic 2 Virtualization Technologies (Labs 6–9)
• Day 3 — Network Infrastructure — Layer 2, EIGRP/OSPF/BGP and IP services
– Topic 3 Network Infrastructure — Layer 2 and Layer 3 (Labs 10–18)
• Day 4 — Network Infrastructure (wireless), Network Assurance and Network Security
– Topic 3 Network Infrastructure — wireless and IP services (Labs 19–21)
– Topic 4 Network Assurance (Labs 22–25)
– Topic 5 Network Security (Labs 26–30)
• Day 5 — Network Automation, revision and final assessment
– Topic 6 Network Automation (Labs 31–35)
– Revision · TRAQOM Survey · Digital Attendance (Assessment)
– Final Assessment (WA 1 hr + PP 1 hr)
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
15

## Slide 16
SET UP BEFORE WE START
Your Lab Environment
1
Cisco Packet Tracer 8.2+
The primary lab environment. Every .pkt/.pka topology in labs/ opens in Packet Tracer — free from the Cisco Networking Academy.
2
Cisco IOS / IOS XE CLI
All configuration is done at the IOS CLI, so the commands transfer directly to real 9200/9300 switches and ISR/CSR routers.
3
Wireless LAN Controller (WLC)
The Packet Tracer WLC GUI is used for the WLAN, WPA2-Enterprise and wireless troubleshooting labs.
4
Python 3.10+
Used for the automation labs — interpreting scripts, parsing JSON and calling REST APIs.
5
Postman or curl
Used to exercise the Cisco DNA Center and RESTCONF APIs and to read response codes.
6
A text editor
VS Code or any editor for writing Python scripts, JSON payloads and saved configurations.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
16

## Slide 17
BEFORE YOU START
Briefing for Assessment
1
Do · Clear your desk
Place phones and other materials under the table or on the floor.
2
Don't · No recording
No photos or recording of assessment scripts.
3
Don't · No discussion
Work individually — no discussion during the assessment.
4
Do · Black or blue pen
Use a black or blue pen for hard-copy assessments.
5
Don't · No correction fluid
No liquid paper or correction tape may be used.
6
Do · Stop on time
Scripts are collected when time is up.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
17

## Slide 18
FINAL ASSESSMENT
Final Assessment
1
Written Assessment (WA)
Short-Answer Questions (SAQ) · 1 hour · open book. Tests the underpinning knowledge taught in the slides.
2
Practical Performance (PP)
Hands-on Cisco configuration and verification tasks · 1 hour · open book. Tests the ability you built in the labs.
3
Open book
You may use the course slides, the Learner Guide and approved materials only.
4
Eligibility
A minimum of 75% attendance is required to be eligible for assessment and funding.
5
Result
You are assessed as Competent (C) or Not Yet Competent (NYC) on each instrument.
6
Appeals
An appeal process is available if you wish to contest an assessment outcome.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
18

## Slide 19
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey
Scan the QR code on the LMS
2
Digital attendance
Scan the SSG assessment QR
3
Sit WA then PP
Open book · 1 hour each
4
Submit on the LMS
Upload your completed answers
5
Sign the record
Sign the Assessment Summary Record
REMEMBER
All five steps are mandatory for WSQ funding — missing the digital attendance or the TRAQOM survey can invalidate your claim.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
19

## Slide 20
WSQ FUNDING
Criteria for Funding
1
Attendance
A minimum attendance rate of 75%, based on the SSG Digital Attendance record.
2
Assessment
Complete both assessment components and be assessed as 'Competent'.
3
Digital attendance
Scan the SSG QR code for AM, PM and Assessment on every training day.
4
TRAQOM survey
Complete the mandatory TRAQOM course feedback survey on the LMS.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
20

## Slide 21
PRACTICE EXAM · exams.tertiaryinfotech.com
Practice Exam — Cisco CCNP ENCOR 350-401
1
200 original questions
Two full practice exams of 100 questions each, written for this blueprint — not redistributed exam content.
2
120 minutes each
The same duration as the real 350-401 exam, so you practise the pacing as well as the content.
3
All six domains
Architecture 15% · Virtualization 10% · Infrastructure 30% · Assurance 10% · Security 20% · Automation 15%.
4
Practice mode
Answers and full explanations revealed immediately after each question — use this while you learn.
5
Exam mode
Timed, answers hidden until you submit, progress saved automatically — use this in the final week.
6
Try it free
exams.tertiaryinfotech.com/practice-exams/cisco/cisco-ccnp-encor — a free sample exam needs no payment details.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
21

## Slide 22
exams.tertiaryinfotech.com/practice-exams/cisco/cisco-ccnp-encor
Practise until the pacing is automatic.
Take the practice exam in Practice mode while you learn, then in Exam mode against the clock. 100 questions in 120 minutes leaves about 72 seconds per question — the pacing is what catches people out, not the content.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
22

## Slide 23
CORE CONCEPTS
The Enterprise Network Core, End to End
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
23

## Slide 24
WHAT YOU ARE PREPARING FOR
ENCOR is one exam across six domains.
350-401 tests whether you can implement core enterprise network technologies — dual-stack architecture, virtualization, infrastructure, assurance, security and automation. This course walks all six, in blueprint order, with a lab for every objective.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
24

## Slide 25
EXAM STRUCTURE
The ENCOR 350-401 Exam at a Glance
1
120 minutes
The exam runs two hours and is the core exam for both CCNP Enterprise and CCIE Enterprise.
2
Six domains
Architecture, Virtualization, Infrastructure, Network Assurance, Security and Automation.
3
Dual stack throughout
IPv4 and IPv6 are both examinable — OSPFv3 and IPv6 addressing appear alongside their v4 equivalents.
4
Configure, verify, describe
Read the verb in each objective: 'configure and verify' means hands-on, 'describe' means conceptual.
5
Core plus concentration
Passing ENCOR alone earns the Cisco Certified Specialist – Enterprise Core certification.
6
Then a concentration
CCNP Enterprise needs ENCOR plus one concentration exam such as ENARSI.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
25

## Slide 26
HOW TO STUDY THE BLUEPRINT
Read the Verb — What Each Objective Actually Asks
Verb in the blueprint
What the exam expects
Example objective
How this course covers it
Configure and verify
Hands-on configuration and the show command that proves it
Configure and verify eBGP
A full lab with the commands and the verification
Troubleshoot
Find and fix a broken configuration
Troubleshoot static and dynamic EtherChannels
A lab that starts broken, not blank
Describe
Explain the concept and its components
Describe REST API security
A concept walkthrough and a review worksheet
Interpret
Read a given configuration or script and predict the result
Interpret basic Python components
Predict-then-run exercises
Compare
State the differences and when to choose each
Compare agent vs agentless tools
A comparison matrix plus a justified recommendation
WHEN IT MATTERS The verb tells you how deep to go. 'Describe' will never ask you for a command; 'configure and verify' always will.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
26

## Slide 27
THE JOURNEY THIS COURSE FOLLOWS
How a Packet Crosses the Enterprise Core
1
Access
Host attaches, VLAN assigned
2
Distribution
L2 becomes L3, policy applied
3
Core
High-speed transit only
4
WAN edge
NAT, IPsec, SD-WAN
5
Destination
Remote site or cloud
THE POINT
Every topic in this course is one stage of this journey. Keep this picture in mind — the exam questions are almost always about one hop on it.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
27

## Slide 28
A MODEL YOU WILL USE ALL WEEK
The Three Planes — The Idea Behind Every Topic
1
Data plane
Forwards packets. CEF, the FIB and the adjacency table live here, and it runs in hardware at line rate.
2
Control plane
Decides where packets should go. Routing protocols, STP and LISP live here, and it runs in software on the CPU.
3
Management plane
How you configure and monitor the device. SSH, SNMP, NETCONF and RESTCONF live here.
4
Why it matters
CoPP protects the control plane from the data plane, SD-WAN separates them onto different devices, and 'the control plane is down' means something very different from 'the data plane is down'.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
28

## Slide 29
CORE CONCEPTS · THE MODEL BEHIND EVERY TOPIC
The Three Planes of a Network Device
Every topic this week sits in one of these three planes. Know which plane a symptom belongs to and you have already halved the troubleshooting.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
29

## Slide 30
ENCOR 1.6 · HARDWARE AND SOFTWARE SWITCHING
Switching Mechanisms — Process, Fast and CEF
Mechanism
How it decides
Speed
Where the decision is cached
Process switching
Every packet examined by the CPU
Slowest
Nowhere — recomputed each packet
Fast switching
First packet by CPU, rest from cache
Faster
Route cache, built on demand
CEF
FIB built ahead of any traffic
Fastest
FIB + adjacency table, in hardware
WHEN IT MATTERS CEF is the default and the answer to almost every 'which is fastest' question — because it is topology-based, not traffic-driven.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
30

## Slide 31
ENCOR 1.6 · KNOW WHICH TABLE ANSWERS WHICH QUESTION
The Forwarding Tables — CAM, TCAM, RIB, FIB and Adjacency
Table
What it holds
Match type
Populated by
CAM
MAC address to port, per VLAN
Exact match
Learning source MACs from frames
TCAM
ACL, QoS and policy entries
Ternary (masked)
Compiled ACLs and QoS policies
RIB
Best routes from all sources
Longest prefix
Routing protocols and static routes
FIB
CEF's forwarding copy of the RIB
Longest prefix
Built from the RIB by CEF
Adjacency
Layer 2 rewrite for each next hop
Next-hop lookup
ARP and the neighbour tables
WHEN IT MATTERS An exam question naming a MAC address wants CAM; one naming an ACL wants TCAM; one naming a next hop wants the FIB and adjacency pair.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
31

## Slide 32
ENCOR 1.6 · HARDWARE AND SOFTWARE SWITCHING
The Forwarding Tables at a Glance
CEF uses the FIB and the adjacency table together — the FIB decides where, the adjacency table builds the new frame header.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
32

## Slide 33
ENCOR 1.1 · THE DESIGN DECISION
Do You Need a Dedicated Core Layer?
More than about three distribution blocks?
YES — build a 3-tier design
Add a dedicated core. Each distribution block gets two uplinks to the core instead of meshing with every other block, so cabling and complexity grow linearly rather than quadratically.
NO — collapse into 2-tier
Merge core and distribution. Fewer devices, lower cost and less to manage — the right answer for a single building or a small campus.
The trigger is the number of distribution blocks, not the number of users. Four blocks fully meshed need six links; with a core they need four uplinks.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
33

## Slide 34
ENCOR 1.1.a · ENTERPRISE DESIGN PRINCIPLES
Two-Tier vs Three-Tier Campus Design
The design decision is driven by the number of distribution blocks, not the headcount. Beyond roughly three blocks, add the core.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
34

## Slide 35
ENCOR 1.1 · THE SCALING ARGUMENT
Why a Core Layer Scales — Links Needed as Blocks Grow
Chart: 
| 2 blocks | 3 blocks | 4 blocks | 5 blocks | 6 blocks
Full mesh, no core | 1 | 3 | 6 | 10 | 15
With a dedicated core | 2 | 3 | 4 | 5 | 6
WHAT THE DATA SHOWS
Without a core, inter-block links grow as n(n-1)/2 — six blocks need fifteen links. With a core they grow linearly: one uplink per block. This is the whole quantitative case for the third tier.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
35

## Slide 36
ENCOR 1.1.b · HIGH AVAILABILITY TECHNIQUES
High Availability — The Three Layers of Redundancy
1
Hardware redundancy
Dual supervisors, dual power supplies and redundant line cards so a component failure is survivable.
2
Link redundancy
EtherChannel bundles and redundant uplinks so a cable or port failure does not isolate a block.
3
FHRP
HSRP, VRRP or GLBP give hosts one virtual default gateway that survives the failure of the router behind it.
4
SSO / NSF
Stateful switchover keeps the standby supervisor in sync; non-stop forwarding keeps forwarding while routing re-converges.
5
Graceful restart
Neighbours hold the adjacency during a supervisor switchover instead of tearing routing down.
6
Why all four
Each covers a different failure. Redundant hardware without FHRP still leaves hosts pointing at a dead gateway.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
36

## Slide 37
ENCOR 3.4.c · FHRP
First Hop Redundancy Protocols Compared
HSRP
VRRP
GLBP
Standard
Cisco proprietary
IEEE / RFC 5798
Cisco proprietary
Roles
Active / Standby
Master / Backup
AVG / AVF
Default priority
100
100
100
Preemption
Disabled by default
Enabled by default
Enabled by default
Load balancing
No — one active router
No — one master
Yes — across all forwarders
WHEN IT MATTERS The preemption default is the classic exam trap: configure HSRP priority without 'standby preempt' and the higher-priority router will never take over.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
37

## Slide 38
ENCOR 1.5 · QoS COMPONENTS
QoS — Mark Once, at the Trust Boundary
1
Classification
Identify the traffic — by ACL, by protocol, or by the marking a trusted device already applied.
2
Marking
Write the class into the packet: DSCP in the IP header, CoS in the 802.1Q tag. Voice is EF (46).
3
Queuing and scheduling
Decide who transmits next. LLQ gives voice a strict-priority queue; CBWFQ shares the rest by weight.
4
Congestion avoidance
WRED drops selectively before the queue is full, so TCP backs off gradually instead of all at once.
5
Policing
Enforces a rate by dropping or remarking excess — bursty, no delay added.
6
Shaping
Enforces a rate by buffering excess — smooth, but adds delay. Shape towards the provider, police from them.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
38

## Slide 39
ENCOR 1.5 · WORKED EXAMPLE
Reading a QoS Policy Map
Every QoS configuration you will meet has this same three-part shape — learn to read it once.
class-map match-all VOICE
match ip dscp ef
!
class-map match-all VIDEO
match ip dscp af41
!
policy-map WAN-EDGE
class VOICE
priority percent 10
class VIDEO
bandwidth percent 30
class class-default
fair-queue
!
interface Serial0/0/0
service-policy output WAN-EDGE
class-map
Classifies — it says WHICH packets belong to this class, and nothing else.
policy-map
Acts — it says WHAT happens to each class: priority, bandwidth or queuing.
priority percent 10
The strict-priority (low-latency) queue. Voice goes here; it is policed to 10% so it cannot starve everything else.
service-policy output
Applies the policy to an interface in one direction. Without this line the policy does nothing at all.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
39

## Slide 40
ENCOR 1.2 · WIRELESS NETWORK DESIGN
Wireless Design Principles
1
Centralized
All client traffic tunnels to a central WLC over CAPWAP. Simple policy, but the WLC is in every data path.
2
Distributed / FlexConnect
The AP switches client traffic locally at the branch and only sends control traffic to the WLC — right when the WAN is slow or expensive.
3
Controller-less
Mobility Express embeds the controller in an AP. Suits a small site with no room for a separate WLC.
4
Cloud-managed
Meraki-style: management in the cloud, data stays local. Lowest operational overhead.
5
Location services
RSSI trilateration, Angle of Arrival with Hyperlocation, and BLE beacons — accuracy depends on AP density and placement.
6
Client density
High density is a capacity problem: smaller cells, lower transmit power, narrower channels and band steering to 5 GHz.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
40

## Slide 41
ENCOR 3.3.c · AP DISCOVERY AND JOIN
The AP Join Process — CAPWAP End to End
UDP 5246 carries the DTLS-encrypted control tunnel; UDP 5247 carries client data. Both port numbers are directly examinable.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
41

## Slide 42
ENCOR 3.3.c · AP DISCOVERY AND JOIN
How an AP Joins a Controller — CAPWAP
1
Get an address
AP boots and takes DHCP
2
Discover the WLC
Broadcast, option 43, DNS or stored list
3
Select one
By priority, then lowest AP load
4
Join over DTLS
Control tunnel on UDP 5246
5
Download and serve
Image, config, then data on UDP 5247
EXAM POINT
Learn the discovery order and both port numbers — 5246 control, 5247 data. 'The AP will not join' questions are almost always option 43, DNS, or a DTLS certificate mismatch.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
42

## Slide 43
ENCOR 1.3 · SD-WAN CONTROL AND DATA PLANES
Cisco SD-WAN — The Four Planes and What Breaks
Only vBond must be publicly reachable. A vSmart outage stops NEW route learning — it does not stop traffic already flowing.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
43

## Slide 44
ENCOR 1.3 · SD-WAN CONTROL AND DATA PLANES
Cisco SD-WAN — The Four Planes
1
vBond · Orchestration
Authenticates every device and introduces them to each other. The only element that must have a public address.
2
vSmart · Control
Distributes routes and policy over OMP. It never carries user data.
3
vManage · Management
The GUI, the API and the configuration templates. Where you actually operate the fabric.
4
vEdge / cEdge · Data
The routers at each site that build the IPsec fabric and forward the traffic.
5
If vSmart fails
Existing data plane tunnels keep forwarding — but no new routes or policy are learned.
6
If vManage fails
The fabric keeps running; you lose management and monitoring, not forwarding.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
44

## Slide 45
ENCOR 1.4 · SD-ACCESS CONTROL AND DATA PLANES
Cisco SD-Access — Underlay, Overlay and Policy
1
Underlay
Any routed IP network that provides reachability between fabric nodes. It carries no client state.
2
Overlay data plane
VXLAN. The VNI replaces the VLAN as the segment identifier, lifting the ceiling from 4,094 to 16 million.
3
Control plane
LISP. The map server and map resolver answer 'where is this endpoint right now'.
4
Policy plane
TrustSec. An SGT is applied at ingress and enforced as an SGACL at egress — policy follows identity, not IP.
5
Fabric roles
Control plane node, border node, edge node and the wireless LAN controller.
6
Why it matters
Because the endpoint keeps its IP when it roams, policy and mobility both stop depending on the subnet.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
45

## Slide 46
ENCOR 1.4 · SD-ACCESS CONTROL AND DATA PLANES
Cisco SD-Access — The Full Stack
LISP resolves where an endpoint is, VXLAN carries the frame there, and TrustSec decides whether it is allowed.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
46

## Slide 47
ENCOR 1.3 AND 1.4
SD-WAN and SD-Access — Do Not Confuse Them
Cisco SD-WAN
Cisco SD-Access
Where it applies
The WAN, between sites
The campus, inside a site
Control plane
OMP via vSmart
LISP via the control plane node
Data plane
IPsec tunnels
VXLAN
Policy
Centralised and localised policy in vManage
SGTs enforced by TrustSec
Managed by
vManage
Cisco DNA Center
WHEN IT MATTERS Both are 'software-defined' and both appear in domain 1, but they solve different problems in different places. Exam questions rely on you keeping them apart.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
47

## Slide 48
TOPIC 01
Enterprise Architecture
Design principles · wireless design · SD-WAN · SD-Access · QoS · switching mechanisms
01
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
48

## Slide 49
TOPIC 01 · SCOPE
Topic 01 — What This Domain Covers
1
Exam domain
ENCOR domain 1.0 Architecture
2
Exam weighting
15% of the ENCOR 350-401 exam
3
TSC mapping
Skills Framework K1, A1 · Network Configuration (ICT-DIT-3009-1.1)
4
Hands-on labs
Labs 1–5 — every objective has a lab
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
49

## Slide 50
TOPIC WEIGHTING 15%
Key Concepts — Enterprise Architecture
1
Enterprise campus designs are layered: a 2-tier (collapsed core) design merges core and distribution and suits a single building, while a 3-tier design keeps a dedicated core and is justified once you exceed roughly three distribution blocks.
2
The access layer terminates end devices and enforces port security, PoE and QoS trust; the distribution layer aggregates and is the boundary where Layer 2 becomes Layer 3; the core is a high-speed, low-latency transit fabric that must never run policy.
3
High availability is delivered in three planes: redundancy of hardware and links, FHRP (HSRP, VRRP, GLBP) for default-gateway resilience, and SSO/NSF so a supervisor failover does not tear down routing adjacencies.
4
Wireless deployment models trade control against latency — centralized (all traffic tunnelled to a WLC), distributed/FlexConnect (locally switched at the branch), controller-less (Mobility Express), cloud-managed (Meraki) and remote branch.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
50

## Slide 51
TOPIC WEIGHTING 15%
Key Concepts — Enterprise Architecture (2)
1
Location services (RSSI trilateration, Angle of Arrival with Hyperlocation, BLE beacons) drive asset tracking and analytics; accuracy depends on AP density and placement, not on client radio power.
2
Client density planning is a capacity problem, not a coverage problem: high-density areas need smaller cells, lower AP transmit power, narrower channel widths and band steering to 5 GHz.
3
Cisco SD-WAN separates a control plane (vSmart), an orchestration plane (vBond), a management plane (vManage) and a data plane (vEdge/cEdge) — OMP distributes routes and policy, and IPsec builds the fabric.
4
Cisco SD-Access builds a VXLAN overlay on any IP underlay: the control plane is LISP (map server / map resolver), the data plane is VXLAN, and policy is carried as SGTs enforced by TrustSec.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
51

## Slide 52
TOPIC WEIGHTING 15%
Key Concepts — Enterprise Architecture (3)
1
QoS components are classification and marking (DSCP/CoS), queuing and scheduling (LLQ/CBWFQ), congestion avoidance (WRED), policing (drops) and shaping (buffers) — mark once, at the trust boundary, and act everywhere.
2
Wireless QoS maps DSCP to the 802.11e user-priority (WMM) access categories; a mismatch between the wired DSCP and the wireless UP is the most common reason voice quality collapses over Wi-Fi.
3
Hardware switching is a table story: CAM is exact-match (MAC address table), TCAM is ternary and stores masked entries for ACLs and QoS, the FIB is the CEF-prepared copy of the RIB, and the adjacency table holds the rewrite information.
4
Cisco Express Forwarding replaces process and fast switching by building the FIB and adjacency table ahead of traffic — so the first packet of a flow is switched in hardware just like the millionth.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
52

## Slide 53
WHAT YOU'LL DO
Hands-On Labs — Enterprise Architecture
Labs 1–2
• Investigate the CAM and TCAM Tables
• Analyse Cisco Express Forwarding
Labs 3–4
• Compare Two-Tier and Three-Tier Campus Designs
• Interpret Wired and Wireless QoS Configurations
Lab 5
• Explore SD-WAN and SD-Access Architecture
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
53

## Slide 54
TOPIC 01 · HANDS-ON
Investigate the CAM and TCAM Tables
LAB 1
Describe hardware switching mechanisms such as CAM, TCAM, FIB, RIB and adjacency tables (ENCOR 1.6).
You take the role of a campus network engineer verifying how an access switch actually forwards a frame. You generate traffic between hosts, watch the MAC address table (CAM) populate by learning source addresses, then age an entry out and observe the switch flood the unknown unicast. You finish by inspecting how TCAM stores the masked ACL and QoS entries that CAM's exact-match lookup cannot hold.
YOU'LL BUILD
A documented CAM table showing dynamically learned entries, one static entry you added, and a written comparison of CAM versus TCAM lookup behaviour.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, S1/S2 access switches, PC-A and PC-B
DONE WHEN
'show mac address-table dynamic' lists both PC MAC addresses against the correct ports and VLAN 10, 'show mac address-table static' shows your pinned entry, and you can state that CAM does exact-match on MAC while TCAM does masked match for ACL/QoS.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
54

## Slide 55
LAB 1 · PROCESS MAP
How Lab 1 Runs
1
Open lab-01-cam-tcam/lab-01-cam-tcam.pkt and confirm PC-A (192.168.10.10) and PC-B (192.168.10.20) are in VLAN 10
2
Clear the switch MAC address table so you start from a known empty state
S1# clear mac address-table dynamic
3
Display the empty table and note that only the CPU entries remain
S1# show mac address-table
4
From PC-A, ping PC-B to make the switch learn both source MAC addresses
C:\> ping 192.168.10.20
5
Display the CAM table again and record the two dynamic entries, their VLAN and their ports
S1# show mac address-table dynamic
THE POINT
Describe hardware switching mechanisms such as CAM, TCAM, FIB, RIB and adjacency tables (ENCOR 1.6).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
55

## Slide 56
LAB 1 · VERIFY
Investigate the CAM and TCAM Tables
✅ Expected result
'show mac address-table dynamic' lists both PC MAC addresses against the correct ports and VLAN 10, 'show mac address-table static' shows your pinned entry, and you can state that CAM does exact-match on MAC while TCAM does masked match for ACL/QoS.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
56

## Slide 57
TOPIC 01 · HANDS-ON
Analyse Cisco Express Forwarding
LAB 2
Describe and verify CEF, the FIB and the adjacency table, and contrast them with process and fast switching (ENCOR 1.6).
Continuing as the campus engineer, you now move up to Layer 3 and prove how the router forwards in hardware. You examine the RIB, then the FIB that CEF builds from it ahead of any traffic, then the adjacency table that holds the Layer 2 rewrite. You disable CEF to watch forwarding fall back to process switching, observe the CPU cost, and re-enable it.
YOU'LL BUILD
A side-by-side record of the RIB, the FIB and the adjacency table for one destination prefix, plus measured evidence of the CPU difference when CEF is disabled.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1 and R2 routers, PC-A and PC-B
DONE WHEN
'show ip cef' returns a populated FIB and 'show adjacency detail' shows a valid rewrite for the next hop; with CEF disabled you can point to a measurably higher CPU figure during the ping, and it falls again once CEF is re-enabled.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
57

## Slide 58
LAB 2 · PROCESS MAP
How Lab 2 Runs
1
Open lab-02-cef/lab-02-cef.pkt and confirm R1 G0/0 is 192.168.10.1 and the R1–R2 link is 10.1.1.0/30
2
Display the routing table (the RIB) — the control plane's view of the network
R1# show ip route
3
Display the FIB that CEF has pre-built from that RIB
R1# show ip cef
4
Look at one specific prefix in the FIB and note its next hop and outgoing interface
R1# show ip cef 192.168.20.0
5
Display the adjacency table holding the Layer 2 rewrite string for that next hop
R1# show adjacency detail
THE POINT
Describe and verify CEF, the FIB and the adjacency table, and contrast them with process and fast switching (ENCOR 1.6).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
58

## Slide 59
LAB 2 · VERIFY
Analyse Cisco Express Forwarding
✅ Expected result
'show ip cef' returns a populated FIB and 'show adjacency detail' shows a valid rewrite for the next hop; with CEF disabled you can point to a measurably higher CPU figure during the ping, and it falls again once CEF is re-enabled.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
59

## Slide 60
TOPIC 01 · HANDS-ON
Compare Two-Tier and Three-Tier Campus Designs
LAB 3
Explain enterprise design principles including 2-tier, 3-tier, fabric and cloud designs (ENCOR 1.1.a).
A 400-staff company on one campus is merging with a 2,000-staff company across four buildings. As the design engineer you must recommend a campus architecture for the merged organisation. You document the current 2-tier collapsed-core design, model the merged requirement, and justify whether a dedicated core layer is now warranted — the exact judgement the exam tests.
YOU'LL BUILD
A completed design comparison table and a one-page written recommendation stating whether to move to a 3-tier design, with the trigger conditions that justify it.
TOOLCHAIN
Cisco Packet Tracer, network diagram, design decision worksheet
DONE WHEN
Your recommendation names 3-tier for the merged network, shows the full-mesh link count that falls from six inter-block links to four uplinks once a core is added, and states that the core layer carries no ACLs or policy.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
60

## Slide 61
LAB 3 · PROCESS MAP
How Lab 3 Runs
1
Open lab-03-campus-design/lab-03-campus-design.pkt and identify which switches are access and which are distribution
2
Record what each layer is doing today — port security and PoE at access, routing at distribution
SW-DIST-1# show ip route
3
Confirm the distribution layer is the Layer 2 to Layer 3 boundary by checking the SVIs
SW-DIST-1# show ip interface brief | include Vlan
4
Count the distribution blocks the merged network will need (one per building)
5
Apply the design rule: a dedicated core is justified beyond roughly three distribution blocks
THE POINT
Explain enterprise design principles including 2-tier, 3-tier, fabric and cloud designs (ENCOR 1.1.a).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
61

## Slide 62
LAB 3 · VERIFY
Compare Two-Tier and Three-Tier Campus Designs
✅ Expected result
Your recommendation names 3-tier for the merged network, shows the full-mesh link count that falls from six inter-block links to four uplinks once a core is added, and states that the core layer carries no ACLs or policy.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
62

## Slide 63
TOPIC 01 · HANDS-ON
Interpret Wired and Wireless QoS Configurations
LAB 4
Interpret wired and wireless QoS configurations, including QoS components and QoS policy (ENCOR 1.5).
Voice calls on the campus wireless network are breaking up during busy periods. As the network engineer you trace the QoS treatment of a voice packet end to end: you read the classification and marking at the wired trust boundary, examine the queuing policy, then check how DSCP maps to the 802.11e WMM access category on the wireless side — where the mismatch usually is.
YOU'LL BUILD
A documented end-to-end QoS policy showing the class map, policy map and service policy, plus the DSCP-to-WMM mapping table that explains the voice degradation.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1 router, SW-1 switch, WLC
DONE WHEN
You can trace a voice packet from the phone's EF marking, through the trusted access port, into the priority queue on the WAN interface, and state which DSCP-to-WMM mapping is wrong and why calls break up.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
63

## Slide 64
LAB 4 · PROCESS MAP
How Lab 4 Runs
1
Open lab-04-qos/lab-04-qos.pkt and locate the IP phone, the access switch and the WAN router
2
Display the class maps that classify traffic into voice, video and best effort
R1# show class-map
3
Display the policy map that assigns bandwidth and priority to each class
R1# show policy-map
4
Identify the low-latency queue reserved for voice — the strict-priority queue
R1# show policy-map interface Serial0/0/0
5
Read the marking: voice should carry DSCP EF (46), call signalling CS3 (24), video AF41 (34)
R1# show policy-map interface | include dscp
THE POINT
Interpret wired and wireless QoS configurations, including QoS components and QoS policy (ENCOR 1.5).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
64

## Slide 65
LAB 4 · VERIFY
Interpret Wired and Wireless QoS Configurations
✅ Expected result
You can trace a voice packet from the phone's EF marking, through the trusted access port, into the priority queue on the WAN interface, and state which DSCP-to-WMM mapping is wrong and why calls break up.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
65

## Slide 66
TOPIC 01 · HANDS-ON
Explore SD-WAN and SD-Access Architecture
LAB 5
Explain the working principles of the Cisco SD-WAN and SD-Access solutions and their control and data plane elements (ENCOR 1.3, 1.4).
Your organisation is evaluating both Cisco SD-WAN for its branch WAN and SD-Access for its campus. As the architect you must be able to name every plane element and say what breaks if it fails. You map the four SD-WAN planes and the SD-Access LISP/VXLAN/TrustSec stack, then work through failure scenarios that the exam poses as 'what happens if…' questions.
YOU'LL BUILD
Two completed architecture maps — SD-WAN's four planes and SD-Access's control/data/policy planes — plus a failure-impact table for each component.
TOOLCHAIN
Cisco Packet Tracer, architecture worksheet, sdwan-components.csv, sdaccess-components.csv
DONE WHEN
You can name all four SD-WAN planes with their controller, state that a vSmart outage stops new route learning but not existing forwarding, and correctly identify LISP as the SD-Access control plane and VXLAN as its data plane.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
66

## Slide 67
LAB 5 · PROCESS MAP
How Lab 5 Runs
1
Open lab-05-sdwan-sdaccess/ and read the two topology diagrams provided
2
Map the SD-WAN orchestration plane to vBond and state what it does — authenticates and introduces devices
3
Map the control plane to vSmart and note it distributes routes and policy over OMP, never carrying data
4
Map the management plane to vManage — the GUI, API and configuration templates
5
Map the data plane to the vEdge/cEdge routers that build the IPsec fabric between sites
THE POINT
Explain the working principles of the Cisco SD-WAN and SD-Access solutions and their control and data plane elements (ENCOR 1.3, 1.4).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
67

## Slide 68
LAB 5 · VERIFY
Explore SD-WAN and SD-Access Architecture
✅ Expected result
You can name all four SD-WAN planes with their controller, state that a vSmart outage stops new route learning but not existing forwarding, and correctly identify LISP as the SD-Access control plane and VXLAN as its data plane.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
68

## Slide 69
TOPIC RECAP
Recap — Enterprise Architecture
• You can now: Describe hardware switching mechanisms such as CAM, TCAM, FIB, RIB and adjacency tables (ENCOR 1.6).
• You can now: Describe and verify CEF, the FIB and the adjacency table, and contrast them with process and fast switching (ENCOR 1.6).
• You can now: Explain enterprise design principles including 2-tier, 3-tier, fabric and cloud designs (ENCOR 1.1.a).
• You can now: Interpret wired and wireless QoS configurations, including QoS components and QoS policy (ENCOR 1.5).
• You can now: Explain the working principles of the Cisco SD-WAN and SD-Access solutions and their control and data plane elements (ENCOR 1.3, 1.4).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
69

## Slide 70
TOPIC 02
Virtualization Technologies
Hypervisors · virtual machines · virtual switching · VRF · GRE and IPsec · LISP and VXLAN
02
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
70

## Slide 71
TOPIC 02 · SCOPE
Topic 02 — What This Domain Covers
1
Exam domain
ENCOR domain 2.0 Virtualization
2
Exam weighting
10% of the ENCOR 350-401 exam
3
TSC mapping
Skills Framework K2, A2 · Network Configuration (ICT-DIT-3009-1.1)
4
Hands-on labs
Labs 6–9 — every objective has a lab
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
71

## Slide 72
TOPIC WEIGHTING 10%
Key Concepts — Virtualization Technologies
1
A Type 1 (bare-metal) hypervisor such as ESXi, KVM or Hyper-V runs directly on the hardware and is what data centres deploy; a Type 2 hypervisor such as VMware Workstation or VirtualBox runs as an application on a host OS and suits a lab.
2
A virtual machine packages vCPU, vRAM, vNIC and virtual disk with a full guest OS — heavier than a container but fully isolated, which is why network functions (CSR 1000v, ASAv, WLC-v) ship as VMs.
3
Virtual switching (vSwitch, Cisco Nexus 1000v, DVS) moves the access layer inside the hypervisor: VM-to-VM traffic on the same host never touches a physical switch, which is exactly why it can bypass your physical ACLs.
4
VRF (Virtual Routing and Forwarding) creates multiple independent routing tables on one device — the same IP prefix can exist in two VRFs without conflict, giving Layer 3 segmentation without extra hardware.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
72

## Slide 73
TOPIC WEIGHTING 10%
Key Concepts — Virtualization Technologies (2)
1
VRF-Lite is VRF without MPLS: you define the VRF, assign interfaces with 'vrf forwarding', and every show/ping/traceroute must then be qualified with 'vrf <name>' or it consults the global table and appears to fail.
2
GRE tunnels are simple, multiprotocol and support routing protocols and multicast — but they provide no confidentiality, integrity or authentication whatsoever.
3
IPsec provides confidentiality, integrity, authentication and anti-replay; the classic enterprise pattern is GRE over IPsec, which gives you the routing and multicast support of GRE plus the protection of IPsec.
4
IPsec negotiates in two phases: IKE Phase 1 builds a bidirectional management tunnel (ISAKMP SA), and Phase 2 builds the unidirectional IPsec SAs that actually carry data — an interesting-traffic ACL mismatch is the classic Phase 2 failure.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
73

## Slide 74
TOPIC WEIGHTING 10%
Key Concepts — Virtualization Technologies (3)
1
LISP splits location from identity: an EID identifies the endpoint and an RLOC identifies where it currently attaches, with a map server / map resolver providing the lookup — this is what makes SD-Access mobility work.
2
VXLAN encapsulates a Layer 2 frame in UDP (port 4789) and carries it across a routed underlay, extending Layer 2 without spanning tree and lifting the segment ceiling from 4,094 VLANs to 16 million VNIs.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
74

## Slide 75
ENCOR 2.3.b · NETWORK VIRTUALIZATION
Decoding the VXLAN Header
Fifty bytes of overhead is why the underlay MTU must be at least 1550 — an underlay left at 1500 silently drops or fragments.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
75

## Slide 76
WHAT YOU'LL DO
Hands-On Labs — Virtualization Technologies
Labs 6–7
• Configure and Verify VRF-Lite
• Configure and Verify a GRE Tunnel
Labs 8–9
• Configure and Verify a Site-to-Site IPsec VPN
• Explore LISP and VXLAN Network Virtualization
—
• —
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
76

## Slide 77
TOPIC 02 · HANDS-ON
Configure and Verify VRF-Lite
LAB 6
Configure and verify data path virtualization technologies — VRF (ENCOR 2.2.a).
Your organisation must keep guest traffic and corporate traffic completely separate on the same physical router, and the acquisition it just completed uses the same 192.168.1.0/24 range as head office. As the network engineer you solve both problems with VRF-Lite: two independent routing tables on one device, with overlapping address space and no leaking between them.
YOU'LL BUILD
A router carrying two VRFs (CORP and GUEST) with overlapping 192.168.1.0/24 prefixes, proven isolated by a VRF-aware ping that succeeds inside a VRF and fails across VRFs.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1 router, CORP-PC and GUEST-PC
DONE WHEN
'show vrf' lists CORP and GUEST with their interfaces, both VRF routing tables carry 192.168.1.0/24 independently, 'ping vrf CORP' succeeds, and the unqualified ping fails — proving isolation rather than a broken configuration.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
77

## Slide 78
LAB 6 · PROCESS MAP
How Lab 6 Runs
1
Open lab-06-vrf-lite/lab-06-vrf-lite.pkt and note both PCs use 192.168.1.10 in different VRFs
2
Create the CORP VRF on R1
R1(config)# vrf definition CORP
3
Enable IPv4 address family inside the VRF
R1(config-vrf)# address-family ipv4
4
Create the GUEST VRF the same way
R1(config)# vrf definition GUEST
5
Assign G0/0 to the CORP VRF — note this clears any existing IP address
R1(config-if)# vrf forwarding CORP
THE POINT
Configure and verify data path virtualization technologies — VRF (ENCOR 2.2.a).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
78

## Slide 79
LAB 6 · VERIFY
Configure and Verify VRF-Lite
✅ Expected result
'show vrf' lists CORP and GUEST with their interfaces, both VRF routing tables carry 192.168.1.0/24 independently, 'ping vrf CORP' succeeds, and the unqualified ping fails — proving isolation rather than a broken configuration.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
79

## Slide 80
TOPIC 02 · HANDS-ON
Configure and Verify a GRE Tunnel
LAB 7
Configure and verify data path virtualization technologies — GRE tunneling (ENCOR 2.2.b).
Head office and the branch are connected only across the public internet, but the routing protocol and multicast traffic they need to exchange cannot cross it. As the WAN engineer you build a GRE tunnel that carries those private networks over the public path, then demonstrate the critical limitation the exam always tests: GRE gives you transport, not confidentiality.
YOU'LL BUILD
A working GRE tunnel between RA (64.103.211.2) and RB (209.165.122.2) carrying 192.168.1.0/24 and 192.168.2.0/24, verified up/up with traffic passing.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, RA and RB routers, PCA and PCB
DONE WHEN
'show interfaces Tunnel0' reports Tunnel0 up, line protocol up with the correct source and destination, PCA pings PCB successfully, and you can state that GRE adds no encryption, authentication or integrity.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
80

## Slide 81
LAB 7 · PROCESS MAP
How Lab 7 Runs
1
Open lab-07-gre/lab-07-gre.pkt and confirm RA and RB can reach each other over their public addresses
RA# ping 209.165.122.2
2
Create the tunnel interface on RA
RA(config)# interface Tunnel0
3
Give the tunnel its own private address in the 10.10.10.0/30 transit range
RA(config-if)# ip address 10.10.10.1 255.255.255.252
4
Set the tunnel source to RA's public interface
RA(config-if)# tunnel source Serial0/0/0
5
Set the tunnel destination to RB's public address
RA(config-if)# tunnel destination 209.165.122.2
THE POINT
Configure and verify data path virtualization technologies — GRE tunneling (ENCOR 2.2.b).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
81

## Slide 82
LAB 7 · VERIFY
Configure and Verify a GRE Tunnel
✅ Expected result
'show interfaces Tunnel0' reports Tunnel0 up, line protocol up with the correct source and destination, PCA pings PCB successfully, and you can state that GRE adds no encryption, authentication or integrity.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
82

## Slide 83
TOPIC 02 · HANDS-ON
Configure and Verify a Site-to-Site IPsec VPN
LAB 8
Configure and verify data path virtualization technologies — IPsec tunneling (ENCOR 2.2.b).
The GRE tunnel from the previous lab carries payroll data in clear text, and the audit has flagged it. As the security-minded network engineer you now build a site-to-site IPsec VPN between R1 and R3 across the R2 ISP, working through both IKE phases and proving the tunnel only forms once interesting traffic matches on both ends.
YOU'LL BUILD
A functioning site-to-site IPsec VPN between R1 (192.168.1.0/24) and R3 (192.168.3.0/24) with a formed ISAKMP SA, established IPsec SAs and encrypted packet counters incrementing.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1/R2/R3 routers, PC-A and PC-C
DONE WHEN
'show crypto isakmp sa' shows the peer in QM_IDLE and 'show crypto ipsec sa' shows non-zero '#pkts encaps' and '#pkts decaps' counters that increase with each ping — traffic between the two LANs is genuinely encrypted.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
83

## Slide 84
LAB 8 · PROCESS MAP
How Lab 8 Runs
1
Open lab-08-ipsec-vpn/lab-08-ipsec-vpn.pkt and confirm R1 and R3 reach each other through R2
R1# ping 10.2.2.2
2
Enable the security technology package if the lab image requires it
R1(config)# license boot module c1900 technology-package securityk9
3
Create the IKE Phase 1 policy defining how the management tunnel is protected
R1(config)# crypto isakmp policy 10
4
Set AES encryption, SHA hashing, pre-shared key authentication and DH group 5
R1(config-isakmp)# encryption aes 256
5
Set the pre-shared key and the peer it applies to
R1(config)# crypto isakmp key Cisco123 address 10.2.2.2
THE POINT
Configure and verify data path virtualization technologies — IPsec tunneling (ENCOR 2.2.b).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
84

## Slide 85
LAB 8 · VERIFY
Configure and Verify a Site-to-Site IPsec VPN
✅ Expected result
'show crypto isakmp sa' shows the peer in QM_IDLE and 'show crypto ipsec sa' shows non-zero '#pkts encaps' and '#pkts decaps' counters that increase with each ping — traffic between the two LANs is genuinely encrypted.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
85

## Slide 86
TOPIC 02 · HANDS-ON
Explore LISP and VXLAN Network Virtualization
LAB 9
Describe network virtualization concepts — LISP and VXLAN (ENCOR 2.3.a, 2.3.b).
Your campus is moving to SD-Access, whose entire mobility story rests on LISP and whose data plane is VXLAN. As the network engineer you must be able to trace a packet through both. You walk the LISP map-request and map-reply exchange, follow an endpoint that roams between edge switches, then decode a VXLAN header field by field and calculate the encapsulation overhead.
YOU'LL BUILD
An annotated LISP registration and lookup walkthrough, a completed VXLAN header decode with all field sizes, and a calculated MTU requirement for the underlay.
TOOLCHAIN
Cisco Packet Tracer, packet-decode worksheet, vxlan-header.csv, lisp-mapping.csv
DONE WHEN
You can state the LISP lookup sequence (register, map-request, map-reply, cache), explain why an EID survives a roam, name UDP 4789 as the VXLAN port, and calculate the 50-byte overhead and the 1550-byte minimum underlay MTU.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
86

## Slide 87
LAB 9 · PROCESS MAP
How Lab 9 Runs
1
Open lab-09-lisp-vxlan/ and read the fabric topology showing edge nodes, border node and control plane node
2
Identify the EID — the endpoint identifier, the host's own IP address that never changes as it roams
3
Identify the RLOC — the routing locator, the address of the edge switch the host is attached to now
4
Trace registration: the edge node registers the EID-to-RLOC binding with the map server
5
Trace lookup: an ingress tunnel router sends a map-request to the map resolver
THE POINT
Describe network virtualization concepts — LISP and VXLAN (ENCOR 2.3.a, 2.3.b).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
87

## Slide 88
LAB 9 · VERIFY
Explore LISP and VXLAN Network Virtualization
✅ Expected result
You can state the LISP lookup sequence (register, map-request, map-reply, cache), explain why an EID survives a roam, name UDP 4789 as the VXLAN port, and calculate the 50-byte overhead and the 1550-byte minimum underlay MTU.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
88

## Slide 89
TOPIC RECAP
Recap — Virtualization Technologies
• You can now: Configure and verify data path virtualization technologies — VRF (ENCOR 2.2.a).
• You can now: Configure and verify data path virtualization technologies — GRE tunneling (ENCOR 2.2.b).
• You can now: Configure and verify data path virtualization technologies — IPsec tunneling (ENCOR 2.2.b).
• You can now: Describe network virtualization concepts — LISP and VXLAN (ENCOR 2.3.a, 2.3.b).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
89

## Slide 90
TOPIC 03
Network Infrastructure
Layer 2 · Layer 3 routing · wireless · IP services — the largest exam domain
03
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
90

## Slide 91
TOPIC 03 · SCOPE
Topic 03 — What This Domain Covers
1
Exam domain
ENCOR domain 3.0 Infrastructure
2
Exam weighting
30% of the ENCOR 350-401 exam
3
TSC mapping
Skills Framework K3, A3 · Network Configuration (ICT-DIT-3009-1.1)
4
Hands-on labs
Labs 10–21 — every objective has a lab
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
91

## Slide 92
TOPIC WEIGHTING 30%
Key Concepts — Network Infrastructure
1
An 802.1Q trunk carries multiple VLANs on one link by inserting a 4-byte tag; the native VLAN is sent untagged, and a native-VLAN mismatch between two ends produces VLAN leaking that CDP will warn you about.
2
DTP negotiates trunking automatically, which is convenient and insecure — production practice is to hard-set 'switchport mode trunk' or 'access' and disable negotiation with 'switchport nonegotiate'.
3
EtherChannel bundles up to eight physical links into one logical link; PAgP is Cisco-proprietary (desirable/auto) and LACP is the IEEE 802.3ad standard (active/passive) — two 'auto' or two 'passive' ends will never form a bundle.
4
EtherChannel members must match on speed, duplex, trunk mode, allowed VLAN list and native VLAN — a mismatch on any of these suspends the port, and 'show etherchannel summary' flags it.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
92

## Slide 93
TOPIC WEIGHTING 30%
Key Concepts — Network Infrastructure (2)
1
STP elects a root bridge by lowest bridge ID (priority + MAC), then each non-root switch picks one root port by lowest cumulative path cost, then each segment picks a designated port — every remaining port is blocked.
2
RSTP (802.1w) converges in seconds rather than the 30–50 seconds of legacy STP by using proposal/agreement on point-to-point links, plus alternate and backup port roles that are pre-computed standby paths.
3
MST (802.1s) maps many VLANs onto a few instances so a 1,000-VLAN campus runs two or three spanning trees instead of a thousand — switches only share an MST region when name, revision and VLAN-to-instance map match exactly.
4
STP protection features each defend a different attack: PortFast skips listening/learning on edge ports, BPDU guard shuts a PortFast port that receives a BPDU, root guard prevents a superior BPDU from moving the root, and loop guard covers unidirectional link failures.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
93

## Slide 94
TOPIC WEIGHTING 30%
Key Concepts — Network Infrastructure (3)
1
EIGRP is an advanced distance-vector protocol using DUAL: the successor is the best path, and a feasible successor is a guaranteed loop-free backup that meets the feasibility condition (its reported distance is less than the current feasible distance).
2
OSPF is a link-state protocol: every router floods LSAs, builds an identical LSDB for the area, and independently runs Dijkstra's SPF to compute its own shortest-path tree — cost is the metric, by default reference bandwidth over interface bandwidth.
3
OSPF area types control LSA flooding: a stub area blocks external LSAs (Type 5), a totally stubby area also blocks summaries (Type 3), and NSSA allows local redistribution via Type 7 LSAs that the ABR translates to Type 5.
4
OSPF neighbours only form when hello/dead timers, area ID, subnet mask, authentication and stub flags all match; on broadcast networks a DR and BDR are elected to prevent an n-squared adjacency mesh.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
94

## Slide 95
TOPIC WEIGHTING 30%
Key Concepts — Network Infrastructure (4)
1
eBGP is a path-vector protocol between autonomous systems: it forms TCP 179 sessions with explicitly configured neighbours, and its best-path algorithm evaluates weight, local preference, AS-path length, origin, MED and more — in that order.
2
eBGP peers are normally directly connected and default to a TTL of 1; peering to a loopback therefore requires 'ebgp-multihop' and 'update-source', which is the most common eBGP lab failure.
3
Policy-based routing overrides the routing table for selected traffic using a route-map matched on an ACL, letting you send (say) guest traffic out a different path than the RIB's best path.
4
Wireless Layer 1 is a power budget: RSSI is the received signal strength, SNR is the margin between signal and noise floor, and a healthy data connection wants roughly -67 dBm RSSI and 25 dB SNR.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
95

## Slide 96
TOPIC WEIGHTING 30%
Key Concepts — Network Infrastructure (5)
1
AP modes serve different jobs — local (normal service), FlexConnect (branch local switching), monitor (scanning only), sniffer (packet capture), bridge/mesh, and SE-Connect for spectrum analysis.
2
An AP joins a WLC by CAPWAP: it discovers candidate controllers (broadcast, DHCP option 43, DNS, or a previously learnt list), selects one by priority and AP capacity, then builds a DTLS-encrypted CAPWAP control tunnel on UDP 5246 and a data tunnel on UDP 5247.
3
Layer 2 roaming keeps the client in the same subnet so only the AP association changes; Layer 3 roaming crosses a subnet boundary and requires an anchor/foreign controller tunnel so the client's IP address survives the move.
4
NTP disciplines clocks in a stratum hierarchy so logs, certificates and troubleshooting timelines correlate; PTP (1588) provides sub-microsecond hardware-timestamped accuracy where NTP's millisecond accuracy is not enough.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
96

## Slide 97
TOPIC WEIGHTING 30%
Key Concepts — Network Infrastructure (6)
1
NAT translates a private inside-local address to a public inside-global address; PAT overloads one public address across many hosts by also translating the source port, which is why 'ip nat inside source list 1 interface g0/0 overload' is the ubiquitous branch configuration.
2
First-hop redundancy protocols present one virtual IP and virtual MAC to hosts: HSRP is Cisco (active/standby, group 0 default, preemption off by default), VRRP is the standard (master/backup, preemption on by default), and GLBP additionally load-balances across gateways.
3
Multicast delivers one stream to many receivers: IGMP is how hosts join a group on the LAN, PIM builds the distribution tree between routers, and the Reverse Path Forwarding check discards any multicast packet that did not arrive on the interface the router would use to reach the source.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
97

## Slide 98
ENCOR 3.1.c · SPANNING TREE ENHANCEMENTS
Spanning Tree Protection Features
BPDU guard err-disables the port and must be recovered; root guard's root-inconsistent state clears by itself. That difference is examined.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
98

## Slide 99
WHAT YOU'LL DO
Hands-On Labs — Network Infrastructure
Labs 10–13
• Troubleshoot 802.1Q Trunking and DTP
• Troubleshoot Static and Dynamic EtherChannels
• Configure RSTP and Tune the Spanning Tree
• Configure Multiple Spanning Tree (MST)
Labs 14–17
• Harden the Spanning Tree with PortFast, BPDU Guard and Root Guard
• Compare EIGRP and OSPF Path Selection
• Configure Multiarea OSPFv2 with Summarization and Filtering
• Configure Multiarea OSPFv3 for IPv6
Labs 18–21
• Configure and Verify eBGP
• Configure a Basic WLAN and WPA2-Enterprise on the WLC
• Troubleshoot WLAN and Wireless Client Connectivity
• Configure NTP, NAT/PAT and HSRP
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
99

## Slide 100
TOPIC 03 · HANDS-ON
Troubleshoot 802.1Q Trunking and DTP
LAB 10
Troubleshoot static and dynamic 802.1q trunking protocols (ENCOR 3.1.a).
Users in VLAN 20 on the second floor have lost access to their file server while VLAN 10 users are unaffected. As the support engineer you work the trunk between S1 and S2: you verify the trunk formed at all, check the allowed VLAN list that is silently pruning VLAN 20, and resolve a native VLAN mismatch that CDP is already warning you about in the logs.
YOU'LL BUILD
A repaired 802.1Q trunk carrying VLANs 10, 20 and 99 with a matching native VLAN on both ends, and DTP disabled in favour of a hard-set trunk.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, S1/S2/S3 switches, PC0–PC5
DONE WHEN
'show interfaces trunk' reports mode 'on' with VLANs 10, 20 and 99 allowed and native VLAN 99 on both switches, the mismatch log stops, and the VLAN 20 PC pings its server.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
100

## Slide 101
LAB 10 · PROCESS MAP
How Lab 10 Runs
1
Open lab-10-trunking-dtp/lab-10-trunking-dtp.pkt and confirm PC1 (VLAN 20) cannot reach the server
C:\> ping 192.168.20.1
2
Check whether the link between S1 and S2 formed a trunk at all
S1# show interfaces trunk
3
Look at the switchport detail — note the administrative and operational mode differ
S1# show interfaces GigabitEthernet0/1 switchport
4
Read the DTP negotiation state; two 'dynamic auto' ends never form a trunk
S1# show dtp interface GigabitEthernet0/1
5
Hard-set the trunk on S1 rather than relying on negotiation
S1(config-if)# switchport mode trunk
THE POINT
Troubleshoot static and dynamic 802.1q trunking protocols (ENCOR 3.1.a).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
101

## Slide 102
LAB 10 · VERIFY
Troubleshoot 802.1Q Trunking and DTP
✅ Expected result
'show interfaces trunk' reports mode 'on' with VLANs 10, 20 and 99 allowed and native VLAN 99 on both switches, the mismatch log stops, and the VLAN 20 PC pings its server.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
102

## Slide 103
TOPIC 03 · HANDS-ON
Troubleshoot Static and Dynamic EtherChannels
LAB 11
Troubleshoot static and dynamic EtherChannels — PAgP and LACP (ENCOR 3.1.b).
Three EtherChannel bundles were configured across the distribution layer over the weekend and only one came up. As the engineer on duty you diagnose each: one has both ends passive so LACP never initiates, one has a speed and duplex mismatch that suspends a member port, and one mixes PAgP on one end with LACP on the other — a combination that can never negotiate.
YOU'LL BUILD
Three working EtherChannel bundles — Po1 with PAgP, Po2 with LACP and Po3 negotiated LACP — all showing SU (in use) with every member port bundled.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, S1/S2/S3 switches
DONE WHEN
'show etherchannel summary' shows Po1, Po2 and Po3 all with flags (SU) and every member port marked (P) for bundled — no (s) suspended and no (D) down ports remain.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
103

## Slide 104
LAB 11 · PROCESS MAP
How Lab 11 Runs
1
Open lab-11-etherchannel/lab-11-etherchannel.pkt and check the state of all three port channels
S1# show etherchannel summary
2
Read the flags column — SU means in use, SD means down, and (s) means suspended
3
Investigate Po2 where both ends were left passive
S1# show etherchannel 2 port-channel
4
Set S1's end of Po2 to LACP active so one side initiates
S1(config-if-range)# channel-group 2 mode active
5
Confirm the S2 end stays passive — active-to-passive is a valid LACP pairing
S2# show etherchannel summary
THE POINT
Troubleshoot static and dynamic EtherChannels — PAgP and LACP (ENCOR 3.1.b).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
104

## Slide 105
LAB 11 · VERIFY
Troubleshoot Static and Dynamic EtherChannels
✅ Expected result
'show etherchannel summary' shows Po1, Po2 and Po3 all with flags (SU) and every member port marked (P) for bundled — no (s) suspended and no (D) down ports remain.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
105

## Slide 106
TOPIC 03 · HANDS-ON
Configure RSTP and Tune the Spanning Tree
LAB 12
Configure and verify common Spanning Tree Protocols — RSTP — and Spanning Tree enhancements (ENCOR 3.1.c).
The spanning tree in the distribution block elected an access switch as root, so traffic between two distribution switches is taking a suboptimal path through the wiring closet. As the engineer you deterministically move the root where it belongs, tune the port costs, migrate the network from legacy PVST+ to Rapid PVST+, and measure the convergence improvement.
YOU'LL BUILD
A spanning tree with S1 as the deterministic root bridge and S2 as the secondary, running Rapid PVST+, with a measured convergence time on link failure.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, S1/S2/S3 switches, PC-A
DONE WHEN
'show spanning-tree vlan 1' on S1 states 'This bridge is the root' with priority 4096, all switches report protocol rstp, and your recorded convergence after the link failure is seconds rather than the 30–50 seconds of legacy STP.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
106

## Slide 107
LAB 12 · PROCESS MAP
How Lab 12 Runs
1
Open lab-12-rstp/lab-12-rstp.pkt and identify which switch is currently root for VLAN 1
S1# show spanning-tree vlan 1
2
Note the root bridge ID and compare it with each switch's own bridge ID
S1# show spanning-tree vlan 1 | include Root ID|Bridge ID
3
Record which ports are root, designated and blocking across the three switches
S1# show spanning-tree vlan 1 | include Desg|Root|Altn
4
Make S1 the primary root using the macro, which sets a priority below the current root
S1(config)# spanning-tree vlan 1 root primary
5
Make S2 the secondary root so failover is also deterministic
S2(config)# spanning-tree vlan 1 root secondary
THE POINT
Configure and verify common Spanning Tree Protocols — RSTP — and Spanning Tree enhancements (ENCOR 3.1.c).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
107

## Slide 108
LAB 12 · VERIFY
Configure RSTP and Tune the Spanning Tree
✅ Expected result
'show spanning-tree vlan 1' on S1 states 'This bridge is the root' with priority 4096, all switches report protocol rstp, and your recorded convergence after the link failure is seconds rather than the 30–50 seconds of legacy STP.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
108

## Slide 109
TOPIC 03 · HANDS-ON
Configure Multiple Spanning Tree (MST)
LAB 13
Configure and verify common Spanning Tree Protocols — MST (ENCOR 3.1.c).
The campus carries 200 VLANs, and running one spanning tree per VLAN is consuming switch CPU and making troubleshooting impractical. As the engineer you consolidate them onto two MST instances, load-balancing the VLANs across two roots, and confirm all switches join the same MST region — which requires name, revision and VLAN map to match exactly.
YOU'LL BUILD
A three-switch MST region named CAMPUS with VLANs mapped to instances 1 and 2, S1 root for instance 1 and S2 root for instance 2, giving true load distribution.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, S1/S2/S3 switches
DONE WHEN
'show spanning-tree mst configuration' returns the same region name CAMPUS, revision 1 and identical configuration digest on all three switches, and 'show spanning-tree mst' shows S1 root for instance 1 and S2 root for instance 2.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
109

## Slide 110
LAB 13 · PROCESS MAP
How Lab 13 Runs
1
Open lab-13-mst/lab-13-mst.pkt and count how many spanning tree instances are running today
S1# show spanning-tree summary
2
Change the spanning tree mode to MST on S1
S1(config)# spanning-tree mode mst
3
Enter MST configuration mode to define the region
S1(config)# spanning-tree mst configuration
4
Name the region — this must match character for character on every switch
S1(config-mst)# name CAMPUS
5
Set the revision number, which must also match exactly
S1(config-mst)# revision 1
THE POINT
Configure and verify common Spanning Tree Protocols — MST (ENCOR 3.1.c).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
110

## Slide 111
LAB 13 · VERIFY
Configure Multiple Spanning Tree (MST)
✅ Expected result
'show spanning-tree mst configuration' returns the same region name CAMPUS, revision 1 and identical configuration digest on all three switches, and 'show spanning-tree mst' shows S1 root for instance 1 and S2 root for instance 2.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
111

## Slide 112
TOPIC 03 · HANDS-ON
Harden the Spanning Tree with PortFast, BPDU Guard and Root Guard
LAB 14
Configure and verify Spanning Tree enhancements such as root guard and BPDU guard (ENCOR 3.1.c).
A contractor plugged a personal switch into a meeting-room wall port last month and became the spanning tree root, black-holing the floor for four minutes. As the engineer you make that impossible: PortFast on edge ports so hosts get an instant link, BPDU guard to shut any edge port that receives a BPDU, and root guard on the distribution uplinks.
YOU'LL BUILD
Edge ports running PortFast with BPDU guard globally enabled, root guard on the distribution-facing uplinks, and a demonstrated err-disable when a rogue BPDU arrives.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, S1/S2/S3 switches, rogue switch, PC-A
DONE WHEN
The rogue switch's BPDU puts the PortFast port into err-disabled with a BPDUGUARD log entry, 'show spanning-tree inconsistentports' reports a root-inconsistent port when a superior BPDU hits the guarded uplink, and errdisable recovery is armed.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
112

## Slide 113
LAB 14 · PROCESS MAP
How Lab 14 Runs
1
Open lab-14-stp-hardening/lab-14-stp-hardening.pkt and time how long a PC port takes to forward
2
Enable PortFast on the access port so it skips listening and learning
S1(config-if)# spanning-tree portfast
3
Enable PortFast by default on all non-trunking ports
S1(config)# spanning-tree portfast default
4
Verify PortFast is active on the interface
S1# show spanning-tree interface FastEthernet0/1 portfast
5
Enable BPDU guard on that specific interface
S1(config-if)# spanning-tree bpduguard enable
THE POINT
Configure and verify Spanning Tree enhancements such as root guard and BPDU guard (ENCOR 3.1.c).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
113

## Slide 114
LAB 14 · VERIFY
Harden the Spanning Tree with PortFast, BPDU Guard and Root Guard
✅ Expected result
The rogue switch's BPDU puts the PortFast port into err-disabled with a BPDUGUARD log entry, 'show spanning-tree inconsistentports' reports a root-inconsistent port when a superior BPDU hits the guarded uplink, and errdisable recovery is armed.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
114

## Slide 115
TOPIC 03 · HANDS-ON
Compare EIGRP and OSPF Path Selection
LAB 15
Compare routing concepts of EIGRP and OSPF — advanced distance vector versus link state, load balancing, path selection, metrics and area types (ENCOR 3.2.a).
Your network runs EIGRP in the legacy branch estate and OSPF in the new campus, and you must explain to management why the two choose different paths across the identical topology. As the engineer you configure both over the same links, compare their metrics, and demonstrate the one capability EIGRP has that OSPF does not: unequal-cost load balancing.
YOU'LL BUILD
Both protocols running over one topology with documented metric calculations, an identified successor and feasible successor in EIGRP, and working unequal-cost load balancing via the variance command.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1/R2/R3 routers
DONE WHEN
'show ip eigrp topology' identifies a successor and at least one feasible successor with its reported distance, the routing table shows two unequal-cost paths after variance 2, and OSPF neighbours reach FULL with a cost you can calculate from reference bandwidth over interface bandwidth.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
115

## Slide 116
LAB 15 · PROCESS MAP
How Lab 15 Runs
1
Open lab-15-eigrp-ospf/lab-15-eigrp-ospf.pkt and review the three-router topology with unequal-bandwidth links
2
Enable EIGRP in named mode on R1
R1(config)# router eigrp CAMPUS
3
Enter the IPv4 unicast address family with autonomous system 100
R1(config-router)# address-family ipv4 unicast autonomous-system 100
4
Advertise the connected networks
R1(config-router-af)# network 172.16.0.0 0.0.255.255
5
Verify the EIGRP neighbours have formed
R1# show ip eigrp neighbors
THE POINT
Compare routing concepts of EIGRP and OSPF — advanced distance vector versus link state, load balancing, path selection, metrics and area types (ENCOR 3.2.a).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
116

## Slide 117
LAB 15 · VERIFY
Compare EIGRP and OSPF Path Selection
✅ Expected result
'show ip eigrp topology' identifies a successor and at least one feasible successor with its reported distance, the routing table shows two unequal-cost paths after variance 2, and OSPF neighbours reach FULL with a cost you can calculate from reference bandwidth over interface bandwidth.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
117

## Slide 118
TOPIC 03 · HANDS-ON
Configure Multiarea OSPFv2 with Summarization and Filtering
LAB 16
Configure simple OSPFv2 environments including multiple normal areas, summarization and filtering (ENCOR 3.2.b).
The campus OSPF domain has grown to a single area carrying 400 routes, and every link flap triggers a full SPF run everywhere. As the engineer you split it into multiple areas, place the ABR correctly, summarise at the area boundary to contain the flooding, and make LAN interfaces passive so no adjacency is ever attempted towards a host.
YOU'LL BUILD
A multiarea OSPFv2 domain with area 0 backbone plus areas 1 and 2, route summarization at the ABR, passive LAN interfaces, and a stub area that blocks external LSAs.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1/R2/R3 routers, PC1/PC2/PC3
DONE WHEN
All OSPF neighbours are FULL, 'show ip ospf' identifies the ABR with interfaces in two areas, the area 1 prefixes appear as one summarised Type 3 LSA in the backbone, and the stub area's database contains no Type 5 external LSAs.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
118

## Slide 119
LAB 16 · PROCESS MAP
How Lab 16 Runs
1
Open lab-16-ospf-multiarea/lab-16-ospf-multiarea.pkt and note R1 172.16.1.1, R2 172.16.2.1, R3 192.168.1.1
2
Start OSPF process 10 on R1 and set the router ID
R1(config)# router ospf 10
3
Set the router ID explicitly to 1.1.1.1
R1(config-router)# router-id 1.1.1.1
4
Place the backbone link into area 0
R1(config-router)# network 172.16.3.0 0.0.0.3 area 0
5
Place the LAN into area 1
R1(config-router)# network 172.16.1.0 0.0.0.255 area 1
THE POINT
Configure simple OSPFv2 environments including multiple normal areas, summarization and filtering (ENCOR 3.2.b).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
119

## Slide 120
LAB 16 · VERIFY
Configure Multiarea OSPFv2 with Summarization and Filtering
✅ Expected result
All OSPF neighbours are FULL, 'show ip ospf' identifies the ABR with interfaces in two areas, the area 1 prefixes appear as one summarised Type 3 LSA in the backbone, and the stub area's database contains no Type 5 external LSAs.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
120

## Slide 121
TOPIC 03 · HANDS-ON
Configure Multiarea OSPFv3 for IPv6
LAB 17
Configure simple OSPFv3 environments including multiple normal areas (ENCOR 3.2.b).
The organisation is dual-stacking, and IPv6 needs its own routing. As the engineer you configure OSPFv3 across three routers, working with the differences that catch people out: OSPFv3 is enabled per interface rather than with network statements, it still needs a 32-bit router ID even though it routes IPv6, and adjacencies form over link-local addresses.
YOU'LL BUILD
A multiarea OSPFv3 domain with RA in area 1, RB in area 0 and RC in area 2, full adjacencies over link-local addresses, and end-to-end IPv6 reachability.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, RA/RB/RC routers
DONE WHEN
'show ipv6 ospf neighbor' shows all neighbours FULL with link-local addresses as the neighbour address, 'show ipv6 route ospf' contains OI inter-area routes, and RA pings RC's LAN across the backbone.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
121

## Slide 122
LAB 17 · PROCESS MAP
How Lab 17 Runs
1
Open lab-17-ospfv3/lab-17-ospfv3.pkt and note the 2001:db8:1::/64 addressing plan
2
Enable IPv6 unicast routing — nothing IPv6 works without it
RA(config)# ipv6 unicast-routing
3
Start the OSPFv3 process
RA(config)# ipv6 router ospf 10
4
Set the 32-bit router ID, still required even though this routes IPv6
RA(config-rtr)# router-id 1.1.1.1
5
Move to the LAN interface and enable OSPFv3 on it directly
RA(config-if)# ipv6 ospf 10 area 1
THE POINT
Configure simple OSPFv3 environments including multiple normal areas (ENCOR 3.2.b).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
122

## Slide 123
LAB 17 · VERIFY
Configure Multiarea OSPFv3 for IPv6
✅ Expected result
'show ipv6 ospf neighbor' shows all neighbours FULL with link-local addresses as the neighbour address, 'show ipv6 route ospf' contains OI inter-area routes, and RA pings RC's LAN across the backbone.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
123

## Slide 124
TOPIC 03 · HANDS-ON
Configure and Verify eBGP
LAB 18
Configure and verify eBGP between directly connected neighbours, including best path selection and neighbour relationships (ENCOR 3.2.c).
ACME is multihoming to two ISP entry points for internet resilience. As the WAN engineer you configure eBGP to both providers, advertise your own prefix, then influence which path inbound and outbound traffic takes — and you deliberately break the session by peering to a loopback without ebgp-multihop, so you recognise the most common eBGP failure in the field.
YOU'LL BUILD
Established eBGP sessions from ACME1 to both ISP entry points, the local prefix advertised and visible in both providers' tables, and a demonstrated path preference change.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, ACME1, OtherCo1, ISP-Entry-1, ISP-Entry-2
DONE WHEN
'show ip bgp summary' shows both neighbours Established with a non-zero prefix count, 'show ip bgp' marks the best path with >, and after the local preference change the best-path marker moves to the preferred provider's route.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
124

## Slide 125
LAB 18 · PROCESS MAP
How Lab 18 Runs
1
Open lab-18-ebgp/lab-18-ebgp.pkt and confirm ACME1 S0/0/0 is 1.1.1.2 peering to 1.1.1.1
ACME1# ping 1.1.1.1
2
Start BGP with ACME's autonomous system number
ACME1(config)# router bgp 65001
3
Define the eBGP neighbour and its remote AS
ACME1(config-router)# neighbor 1.1.1.1 remote-as 65000
4
Advertise the local LAN prefix into BGP
ACME1(config-router)# network 192.168.0.0 mask 255.255.255.0
5
Disable auto-summary so classful summarisation does not surprise you
ACME1(config-router)# no auto-summary
THE POINT
Configure and verify eBGP between directly connected neighbours, including best path selection and neighbour relationships (ENCOR 3.2.c).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
125

## Slide 126
LAB 18 · VERIFY
Configure and Verify eBGP
✅ Expected result
'show ip bgp summary' shows both neighbours Established with a non-zero prefix count, 'show ip bgp' marks the best path with >, and after the local preference change the best-path marker moves to the preferred provider's route.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
126

## Slide 127
TOPIC 03 · HANDS-ON
Configure a Basic WLAN and WPA2-Enterprise on the WLC
LAB 19
Describe AP discovery and join, wireless segmentation with groups, profiles and tags, and configure wireless security features (ENCOR 3.3.c, 3.3.f, 5.4).
The office is deploying its first controller-based wireless network. As the wireless engineer you build the WLC configuration end to end through the GUI: interfaces and VLANs, a PSK guest WLAN, then a WPA2-Enterprise corporate WLAN backed by RADIUS. You watch the AP complete its CAPWAP discovery and join, and confirm clients land in the right VLAN.
YOU'LL BUILD
A WLC with a management interface on 192.168.200.254, a joined LAP, a PSK guest WLAN and a WPA2-Enterprise corporate WLAN authenticating against the RADIUS server at 172.31.1.254.
TOOLCHAIN
Cisco Packet Tracer, WLC-1 GUI, LAP-1, R1, SW1, RADIUS server, wireless hosts
DONE WHEN
The LAP shows as joined and associated in Wireless > All APs, both WLANs appear enabled in the WLAN list, the guest client receives a 192.168.5.x address, and the corporate client authenticates against RADIUS and appears under Monitor > Clients.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
127

## Slide 128
LAB 19 · PROCESS MAP
How Lab 19 Runs
1
Open lab-19-wlc-wlan/lab-19-wlc-wlan.pkt and browse to the WLC at https://192.168.200.254 from the Admin PC
2
Log in to the WLC GUI and review the Monitor summary page
3
Under Controller > Interfaces, create the VLAN 5 dynamic interface for wireless clients
4
Set the interface IP as 192.168.5.254/24 with gateway 192.168.5.1 and the DHCP server address
5
Confirm the AP has completed CAPWAP discovery and joined under Wireless > All APs
THE POINT
Describe AP discovery and join, wireless segmentation with groups, profiles and tags, and configure wireless security features (ENCOR 3.3.c, 3.3.f, 5.4).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
128

## Slide 129
LAB 19 · VERIFY
Configure a Basic WLAN and WPA2-Enterprise on the WLC
✅ Expected result
The LAP shows as joined and associated in Wireless > All APs, both WLANs appear enabled in the WLAN list, the guest client receives a 192.168.5.x address, and the corporate client authenticates against RADIUS and appears under Monitor > Clients.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
129

## Slide 130
TOPIC 03 · HANDS-ON
Troubleshoot WLAN and Wireless Client Connectivity
LAB 20
Troubleshoot WLAN configuration and wireless client connectivity issues using GUI only (ENCOR 3.3.e).
Three separate wireless complaints arrive the same morning: one user cannot see the SSID, one associates but gets no IP address, and one authenticates but cannot reach the internal server. As the wireless support engineer you must resolve all three using the WLC GUI only — no CLI — which is exactly how the exam frames this objective.
YOU'LL BUILD
Three resolved wireless faults with a documented root cause for each: a disabled/misbroadcast WLAN, a wrong interface-to-VLAN mapping, and a RADIUS shared-secret mismatch.
TOOLCHAIN
Cisco Packet Tracer, WLC-1 GUI, LAP-1, RADIUS server, Laptop1 and Laptop2
DONE WHEN
All three clients reach a working state: the SSID is visible and broadcast, the DHCP client holds an address in the correct VLAN, the 802.1X client authenticates, and troubleshooting-log.csv names a distinct root cause for each fault.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
130

## Slide 131
LAB 20 · PROCESS MAP
How Lab 20 Runs
1
Open lab-20-wlan-troubleshoot/lab-20-wlan-troubleshoot.pkt and log in to the WLC GUI as the admin
2
Fault 1: the user cannot see the SSID — check whether the WLAN is enabled under WLANs
3
Check the Broadcast SSID setting on the WLAN's Advanced tab
4
Confirm the WLAN is applied to the AP group or policy tag serving that AP
5
Enable the WLAN and its SSID broadcast, then confirm the client can see it
THE POINT
Troubleshoot WLAN configuration and wireless client connectivity issues using GUI only (ENCOR 3.3.e).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
131

## Slide 132
LAB 20 · VERIFY
Troubleshoot WLAN and Wireless Client Connectivity
✅ Expected result
All three clients reach a working state: the SSID is visible and broadcast, the DHCP client holds an address in the correct VLAN, the 802.1X client authenticates, and troubleshooting-log.csv names a distinct root cause for each fault.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
132

## Slide 133
TOPIC 03 · HANDS-ON
Configure NTP, NAT/PAT and HSRP
LAB 21
Interpret NTP configurations, configure NAT/PAT, and configure first hop redundancy protocols such as HSRP and VRRP (ENCOR 3.4.a, 3.4.b, 3.4.c).
The branch office needs three IP services before it goes live: synchronised time so logs correlate, PAT so its private hosts reach the internet through one public address, and a redundant default gateway so a router failure does not black-hole the LAN. As the branch engineer you configure all three and prove the HSRP failover actually works.
YOU'LL BUILD
A branch router synchronised to an NTP master, PAT translating 192.168.10.0/24 out one public address, and an HSRP group with virtual IP 192.168.1.254 that fails over on preemption.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1/R2/R3 routers, S1/S3 switches, PC-A and PC-B
DONE WHEN
'show ntp status' reports the clock is synchronised, 'show ip nat translations' lists inside-local to inside-global entries with differing ports, and 'show standby brief' shows R1 Active / R3 Standby — with R3 becoming Active and PC-A's ping continuing when R1's interface is shut.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
133

## Slide 134
LAB 21 · PROCESS MAP
How Lab 21 Runs
1
Open lab-21-ip-services/lab-21-ip-services.pkt and review the three service requirements
2
Configure R1 as the NTP master at stratum 3
R1(config)# ntp master 3
3
Point R2 at R1 as its NTP server
R2(config)# ntp server 209.165.200.226
4
Verify the clock synchronised and note the stratum
R2# show ntp status
5
Check the association and confirm the * marks the synchronised peer
R2# show ntp associations
THE POINT
Interpret NTP configurations, configure NAT/PAT, and configure first hop redundancy protocols such as HSRP and VRRP (ENCOR 3.4.a, 3.4.b, 3.4.c).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
134

## Slide 135
LAB 21 · VERIFY
Configure NTP, NAT/PAT and HSRP
✅ Expected result
'show ntp status' reports the clock is synchronised, 'show ip nat translations' lists inside-local to inside-global entries with differing ports, and 'show standby brief' shows R1 Active / R3 Standby — with R3 becoming Active and PC-A's ping continuing when R1's interface is shut.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
135

## Slide 136
TOPIC RECAP
Recap — Network Infrastructure
• You can now: Troubleshoot static and dynamic 802.1q trunking protocols (ENCOR 3.1.a).
• You can now: Troubleshoot static and dynamic EtherChannels — PAgP and LACP (ENCOR 3.1.b).
• You can now: Configure and verify common Spanning Tree Protocols — RSTP — and Spanning Tree enhancements (ENCOR 3.1.c).
• You can now: Configure and verify common Spanning Tree Protocols — MST (ENCOR 3.1.c).
• You can now: Configure and verify Spanning Tree enhancements such as root guard and BPDU guard (ENCOR 3.1.c).
• You can now: Compare routing concepts of EIGRP and OSPF — advanced distance vector versus link state, load balancing, path selection, metrics and area types (ENCOR 3.2.a).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
136

## Slide 137
TOPIC 04
Network Assurance
Diagnostics · NetFlow · SPAN/RSPAN/ERSPAN · IP SLA · DNA Center · NETCONF and RESTCONF
04
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
137

## Slide 138
TOPIC 04 · SCOPE
Topic 04 — What This Domain Covers
1
Exam domain
ENCOR domain 4.0 Network Assurance
2
Exam weighting
10% of the ENCOR 350-401 exam
3
TSC mapping
Skills Framework K5, A4 · Network Configuration (ICT-DIT-3009-1.1)
4
Hands-on labs
Labs 22–25 — every objective has a lab
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
138

## Slide 139
TOPIC WEIGHTING 10%
Key Concepts — Network Assurance
1
Diagnose from the bottom up: ping proves reachability, extended ping proves it from the right source, traceroute locates where the path breaks, and debug shows why — but debug is CPU-expensive and must be scoped.
2
Conditional debugging ('debug interface', 'debug platform condition') restricts output to one interface, one MAC or one IP so you can safely debug on a production device without drowning the console.
3
SNMP polls devices for counters and state: v2c is community-string based and sends everything in clear text, while v3 adds authentication and encryption and is the only version acceptable in production.
4
Syslog messages carry a facility, a severity 0–7 (0 emergency to 7 debugging) and a mnemonic; sending them to a central collector with accurate NTP timestamps is what makes post-incident correlation possible.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
139

## Slide 140
TOPIC WEIGHTING 10%
Key Concepts — Network Assurance (2)
1
Flexible NetFlow is built from three parts: a flow record (the key and non-key fields you want), a flow exporter (where to send it), and a flow monitor (which binds them and is applied to an interface).
2
NetFlow answers 'who is talking to whom, how much and for how long' — it is a summarised conversation record, not a packet capture, so it scales to a whole network where SPAN never could.
3
SPAN copies traffic from a source port or VLAN to a destination port on the same switch, RSPAN carries the copy across a dedicated VLAN to another switch, and ERSPAN encapsulates it in GRE so it can cross a routed network.
4
IP SLA generates synthetic probes — ICMP echo, UDP jitter, HTTP — and measures latency, jitter and loss continuously, so you learn the path degraded before the user calls.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
140

## Slide 141
TOPIC WEIGHTING 10%
Key Concepts — Network Assurance (3)
1
Tracking an IP SLA operation with an object lets you drive real behaviour from measurement: a static route or an HSRP priority can be withdrawn automatically when the probe fails.
2
Cisco DNA Center organises work into four workflows — Design (site hierarchy and settings), Policy (SGTs and access), Provision (push to devices) and Assurance (health scores and issues) — and it is API-first, so anything the GUI does can be automated.
3
NETCONF is an XML-based configuration protocol running over SSH on port 830 with explicit candidate/running datastores and transactional commits, so a partial failure rolls back cleanly.
4
RESTCONF exposes the same YANG models as HTTPS REST on port 443 using GET, POST, PUT, PATCH and DELETE with JSON or XML — simpler for scripts, but without NETCONF's transactional guarantees.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
141

## Slide 142
WHAT YOU'LL DO
Hands-On Labs — Network Assurance
Labs 22–23
• Diagnose Network Problems with Ping, Traceroute and Conditional Debug
• Configure Syslog, SNMP and Flexible NetFlow
Labs 24–25
• Configure SPAN, RSPAN and IP SLA
• Configure NETCONF and RESTCONF and Explore DNA Center Workflows
—
• —
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
142

## Slide 143
TOPIC 04 · HANDS-ON
Diagnose Network Problems with Ping, Traceroute and Conditional Debug
LAB 22
Diagnose network problems using tools such as debugs, conditional debugs, traceroute, ping, SNMP and syslog (ENCOR 4.1).
A user reports the application server is 'sometimes slow and sometimes down'. As the engineer you work the problem methodically from the bottom of the stack up: extended ping from the right source with the right size, traceroute to locate where the path breaks, then a conditional debug scoped to one host so you can safely watch the control plane on a production router.
YOU'LL BUILD
A completed diagnostic record locating the failure to a specific hop, with an extended ping result set, a traceroute trace and safely-scoped conditional debug output.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1/R2/R3 routers, PC-A
DONE WHEN
Your diagnostic record names the exact hop where the path fails, the sweep identifies the largest packet size that succeeds, and 'undebug all' confirms no debug is left running on the device.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
143

## Slide 144
LAB 22 · PROCESS MAP
How Lab 22 Runs
1
Open lab-22-diagnostics/lab-22-diagnostics.pkt and confirm the reported symptom from PC-A
C:\> ping 192.168.3.3
2
Run a basic ping from the router to establish reachability
R1# ping 192.168.3.3
3
Run an extended ping sourced from the LAN interface — the source is what usually matters
R1# ping 192.168.3.3 source GigabitEthernet0/1
4
Test with a large packet and the do-not-fragment bit to expose an MTU problem
R1# ping 192.168.3.3 size 1500 df-bit
5
Sweep a range of packet sizes to find exactly where it breaks
R1# ping 192.168.3.3 size 1400 repeat 5
THE POINT
Diagnose network problems using tools such as debugs, conditional debugs, traceroute, ping, SNMP and syslog (ENCOR 4.1).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
144

## Slide 145
LAB 22 · VERIFY
Diagnose Network Problems with Ping, Traceroute and Conditional Debug
✅ Expected result
Your diagnostic record names the exact hop where the path fails, the sweep identifies the largest packet size that succeeds, and 'undebug all' confirms no debug is left running on the device.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
145

## Slide 146
TOPIC 04 · HANDS-ON
Configure Syslog, SNMP and Flexible NetFlow
LAB 23
Configure and verify Flexible NetFlow, and use SNMP and syslog for diagnosis (ENCOR 4.1, 4.2).
The network has no visibility: when something breaks, nobody can say what changed or who was using the bandwidth. As the engineer you fix that in three layers — syslog to a central collector with accurate timestamps, SNMPv3 for polled state, and Flexible NetFlow to answer who talked to whom, how much and for how long.
YOU'LL BUILD
A router logging to a syslog collector at severity informational, an SNMPv3 user with authentication and encryption, and a Flexible NetFlow monitor applied to an interface producing a populated flow cache.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1/R2 routers, syslog server, SNMP server
DONE WHEN
'show logging' confirms messages are being sent to 192.168.1.100 at informational severity, 'show snmp user' lists the v3 user with SHA and AES, and 'show flow monitor NETFLOW-MONITOR cache' displays flow entries with source, destination and byte counts.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
146

## Slide 147
LAB 23 · PROCESS MAP
How Lab 23 Runs
1
Open lab-23-netflow-syslog/lab-23-netflow-syslog.pkt and locate the syslog and SNMP servers
2
Ensure the clock is right first — logs without accurate time are almost useless
R1(config)# ntp server 209.165.200.226
3
Turn on millisecond timestamps for both logs and debugs
R1(config)# service timestamps log datetime msec
4
Point syslog at the collector
R1(config)# logging host 192.168.1.100
5
Set the trap severity so you capture informational and above
R1(config)# logging trap informational
THE POINT
Configure and verify Flexible NetFlow, and use SNMP and syslog for diagnosis (ENCOR 4.1, 4.2).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
147

## Slide 148
LAB 23 · VERIFY
Configure Syslog, SNMP and Flexible NetFlow
✅ Expected result
'show logging' confirms messages are being sent to 192.168.1.100 at informational severity, 'show snmp user' lists the v3 user with SHA and AES, and 'show flow monitor NETFLOW-MONITOR cache' displays flow entries with source, destination and byte counts.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
148

## Slide 149
TOPIC 04 · HANDS-ON
Configure SPAN, RSPAN and IP SLA
LAB 24
Configure SPAN/RSPAN/ERSPAN and configure and verify IPSLA (ENCOR 4.3, 4.4).
Security has asked for a packet capture of one server's traffic, and the WAN team wants to know when a path degrades before users complain. As the engineer you deliver both: SPAN to mirror the server port to an analyser, RSPAN to carry a copy to an analyser on another switch, and an IP SLA probe with a tracked object that withdraws a static route when the path fails.
YOU'LL BUILD
A working local SPAN session mirroring the server port, an RSPAN session across a dedicated VLAN, and an IP SLA ICMP echo operation with a tracked object driving a static route.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, S1/S2 switches, R1/R2 routers, analyser PC
DONE WHEN
'show monitor session 1' shows an active local SPAN, the RSPAN session appears on both switches using VLAN 199, 'show ip sla statistics' reports successful probes with an RTT, and 'show track 1' reports the object Up with the default route present.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
149

## Slide 150
LAB 24 · PROCESS MAP
How Lab 24 Runs
1
Open lab-24-span-ipsla/lab-24-span-ipsla.pkt and identify the server port and the analyser port
2
Create a local SPAN session with the server port as the source
S1(config)# monitor session 1 source interface FastEthernet0/1 both
3
Set the analyser port as the destination
S1(config)# monitor session 1 destination interface FastEthernet0/24
4
Verify the SPAN session is active and note the source and destination
S1# show monitor session 1
5
Now build RSPAN — first create the dedicated RSPAN VLAN
S1(config)# vlan 199
THE POINT
Configure SPAN/RSPAN/ERSPAN and configure and verify IPSLA (ENCOR 4.3, 4.4).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
150

## Slide 151
LAB 24 · VERIFY
Configure SPAN, RSPAN and IP SLA
✅ Expected result
'show monitor session 1' shows an active local SPAN, the RSPAN session appears on both switches using VLAN 199, 'show ip sla statistics' reports successful probes with an RTT, and 'show track 1' reports the object Up with the default route present.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
151

## Slide 152
TOPIC 04 · HANDS-ON
Configure NETCONF and RESTCONF and Explore DNA Center Workflows
LAB 25
Configure and verify NETCONF and RESTCONF, and describe Cisco DNA Center workflows (ENCOR 4.5, 4.6).
Your team is moving from CLI-by-hand to programmatic configuration. As the automation engineer you enable NETCONF and RESTCONF on the router, retrieve configuration through each, and compare them honestly: NETCONF's transactional datastores against RESTCONF's simpler REST verbs. You then map the four DNA Center workflows onto the tasks your team does manually today.
YOU'LL BUILD
A router with NETCONF-YANG on port 830 and RESTCONF on 443 both enabled and verified, a retrieved interface configuration through each protocol, and a completed DNA Center workflow mapping.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS XE CLI, Python 3, curl or Postman
DONE WHEN
'show netconf-yang sessions' confirms the service is running, the curl call returns HTTP 200 with a JSON interface list, the Python NETCONF script returns the equivalent XML, and dnac-workflows.csv maps all four DNA Center workflows to real tasks.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
152

## Slide 153
LAB 25 · PROCESS MAP
How Lab 25 Runs
1
Open lab-25-netconf-restconf/ and confirm the router has an IP-reachable management interface
2
Create the privileged user the API will authenticate as
R1(config)# username apiuser privilege 15 secret Api123!
3
Generate the RSA key pair that SSH and HTTPS both require
R1(config)# crypto key generate rsa modulus 2048
4
Enable NETCONF-YANG
R1(config)# netconf-yang
5
Enable the HTTPS server that RESTCONF runs on
R1(config)# ip http secure-server
THE POINT
Configure and verify NETCONF and RESTCONF, and describe Cisco DNA Center workflows (ENCOR 4.5, 4.6).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
153

## Slide 154
LAB 25 · VERIFY
Configure NETCONF and RESTCONF and Explore DNA Center Workflows
✅ Expected result
'show netconf-yang sessions' confirms the service is running, the curl call returns HTTP 200 with a JSON interface list, the Python NETCONF script returns the equivalent XML, and dnac-workflows.csv maps all four DNA Center workflows to real tasks.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
154

## Slide 155
TOPIC RECAP
Recap — Network Assurance
• You can now: Diagnose network problems using tools such as debugs, conditional debugs, traceroute, ping, SNMP and syslog (ENCOR 4.1).
• You can now: Configure and verify Flexible NetFlow, and use SNMP and syslog for diagnosis (ENCOR 4.1, 4.2).
• You can now: Configure SPAN/RSPAN/ERSPAN and configure and verify IPSLA (ENCOR 4.3, 4.4).
• You can now: Configure and verify NETCONF and RESTCONF, and describe Cisco DNA Center workflows (ENCOR 4.5, 4.6).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
155

## Slide 156
TOPIC 05
Network Security
Device access control · AAA · ACLs and CoPP · REST API security · wireless security · security design
05
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
156

## Slide 157
TOPIC 05 · SCOPE
Topic 05 — What This Domain Covers
1
Exam domain
ENCOR domain 5.0 Security
2
Exam weighting
20% of the ENCOR 350-401 exam
3
TSC mapping
Skills Framework K4, A6 · Network Configuration (ICT-DIT-3009-1.1)
4
Hands-on labs
Labs 26–30 — every objective has a lab
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
157

## Slide 158
TOPIC WEIGHTING 20%
Key Concepts — Network Security
1
Device access control starts with the lines: console, VTY and AUX each need a password and a login method, and 'transport input ssh' plus 'no ip http server' removes the plaintext paths.
2
Local user authentication with 'username … secret' stores a strong hash (type 8/9 scrypt where supported), whereas 'password' stores a trivially reversible type 7 — never use type 7 for anything that matters.
3
AAA separates Authentication (who are you), Authorization (what may you do) and Accounting (what did you do) — and 'aaa authentication login default group tacacs+ local' keeps a local fallback so a server outage does not lock you out.
4
TACACS+ encrypts the whole payload, uses TCP 49 and separates authentication from authorization, which is why it is preferred for device administration; RADIUS uses UDP, encrypts only the password, and is the standard for network access (802.1X).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
158

## Slide 159
TOPIC WEIGHTING 20%
Key Concepts — Network Security (2)
1
A standard ACL matches source address only and belongs close to the destination; an extended ACL matches source, destination, protocol and port and belongs close to the source so unwanted traffic is dropped early.
2
Every ACL ends in an implicit 'deny any' — an ACL with only permit statements for your management subnet will silently drop everything else, which is the single most common cause of a self-inflicted lockout.
3
Control Plane Policing protects the CPU by applying a QoS policy to the control plane itself, rate-limiting management and routing traffic so a flood of ICMP or SNMP cannot starve the device of the CPU it needs to keep routing.
4
REST API security rests on transport (always HTTPS/TLS), authentication (tokens or OAuth 2.0 rather than embedded credentials), authorization scope, rate limiting, and input validation — and tokens must never be committed to a repository.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
159

## Slide 160
TOPIC WEIGHTING 20%
Key Concepts — Network Security (3)
1
802.1X is a three-party conversation: the supplicant (client), the authenticator (switch or WLC) and the authentication server (RADIUS/ISE); EAPOL carries EAP between supplicant and authenticator, RADIUS carries it onward.
2
WPA2/WPA3 personal uses a pre-shared key, enterprise uses 802.1X; either way the 4-way handshake derives fresh session keys (PTK/GTK) from the PMK, and it is what proves both sides hold the key without ever sending it.
3
WebAuth intercepts the first HTTP request and presents a captive portal — right for guest access, wrong for anything that needs strong identity, and useless for headless devices.
4
MAB (MAC Authentication Bypass) authenticates a device by its MAC address for printers and IP cameras that cannot run a supplicant — it is weak, because a MAC is trivially spoofed, so it is paired with profiling.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
160

## Slide 161
TOPIC WEIGHTING 20%
Key Concepts — Network Security (4)
1
Network security design layers threat defence (IPS/NGIPS), endpoint security (AMP), a next-generation firewall (application-aware, identity-aware), and segmentation with TrustSec SGTs and MACsec link encryption.
2
TrustSec tags traffic with a Security Group Tag at ingress and enforces it as an SGACL at egress, so policy follows identity rather than IP address — which is what makes policy survive DHCP and mobility.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
161

## Slide 162
ENCOR 5.1.b · AUTHENTICATION AND AUTHORIZATION
AAA and 802.1X — Who Talks to Whom
EAPOL runs between supplicant and authenticator; RADIUS carries it onward. Always create the local fallback user BEFORE 'aaa new-model'.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
162

## Slide 163
WHAT YOU'LL DO
Hands-On Labs — Network Security
Labs 26–27
• Configure Secure Device Access with SSH and Strong Passwords
• Implement Local and Server-Based AAA
Labs 28–29
• Configure Extended ACLs to Mitigate Attacks
• Configure Control Plane Policing
Lab 30
• Analyse Wireless Security, REST API Security and Security Design
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
163

## Slide 164
TOPIC 05 · HANDS-ON
Configure Secure Device Access with SSH and Strong Passwords
LAB 26
Configure and verify device access control — lines and local user authentication (ENCOR 5.1.a).
An audit found the branch routers reachable by Telnet with a type 7 password that anyone can decode in seconds. As the engineer you harden device access: strong hashed local credentials, SSH version 2 only, Telnet removed from the VTY lines, an exec timeout, and login blocking so brute force attempts are throttled.
YOU'LL BUILD
A router and switch reachable only by SSHv2 with type 9 hashed local credentials, Telnet disabled, an exec timeout set and login-attempt throttling armed.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, RTA router, SW1 switch, PCA
DONE WHEN
'show ip ssh' reports SSH Enabled version 2.0, Telnet from PCA is refused, SSH with the netadmin account succeeds, and 'show running-config | include username' shows a strong hash rather than a type 7 password.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
164

## Slide 165
LAB 26 · PROCESS MAP
How Lab 26 Runs
1
Open lab-26-secure-access/lab-26-secure-access.pkt and confirm Telnet currently works from PCA
C:\> telnet 172.16.1.1
2
Set the enable secret so the privileged password is hashed, not stored in the clear
RTA(config)# enable secret Str0ngEn@ble!
3
Create a local user with a strong hash rather than a type 7 password
RTA(config)# username netadmin privilege 15 algorithm-type scrypt secret Adm1n!Pass
4
Encrypt any remaining plaintext passwords in the configuration
RTA(config)# service password-encryption
5
Enforce a minimum password length
RTA(config)# security passwords min-length 10
THE POINT
Configure and verify device access control — lines and local user authentication (ENCOR 5.1.a).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
165

## Slide 166
LAB 26 · VERIFY
Configure Secure Device Access with SSH and Strong Passwords
✅ Expected result
'show ip ssh' reports SSH Enabled version 2.0, Telnet from PCA is refused, SSH with the netadmin account succeeds, and 'show running-config | include username' shows a strong hash rather than a type 7 password.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
166

## Slide 167
TOPIC 05 · HANDS-ON
Implement Local and Server-Based AAA
LAB 27
Configure and verify device access control — authentication and authorization using AAA (ENCOR 5.1.b).
Managing local accounts on 200 devices does not scale, and when an administrator leaves nobody can be sure every account is gone. As the engineer you centralise authentication on TACACS+ and RADIUS with AAA — and you deliberately keep a local fallback, because the classic AAA disaster is locking the whole team out when the server is unreachable.
YOU'LL BUILD
Routers authenticating administrators against TACACS+ (192.168.2.2) and RADIUS (192.168.3.2) with a working local fallback, plus authorization and accounting enabled.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1/R2/R3 routers, TACACS+ server, RADIUS server
DONE WHEN
'test aaa group tacacs+' returns a successful authentication, 'show tacacs' shows the server reachable, and with the server link shut you can still log in with the local admin account — proving the fallback works.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
167

## Slide 168
LAB 27 · PROCESS MAP
How Lab 27 Runs
1
Open lab-27-aaa/lab-27-aaa.pkt and note the TACACS+ server at 192.168.2.2 and RADIUS at 192.168.3.2
2
Create the local fallback account BEFORE you enable AAA — this is what saves you
R1(config)# username admin privilege 15 secret Adm1n!Pass
3
Enable the AAA subsystem
R1(config)# aaa new-model
4
Define the TACACS+ server
R1(config)# tacacs server TAC-SRV
5
Set its address
R1(config-server-tacacs)# address ipv4 192.168.2.2
THE POINT
Configure and verify device access control — authentication and authorization using AAA (ENCOR 5.1.b).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
168

## Slide 169
LAB 27 · VERIFY
Implement Local and Server-Based AAA
✅ Expected result
'test aaa group tacacs+' returns a successful authentication, 'show tacacs' shows the server reachable, and with the server link shut you can still log in with the local admin account — proving the fallback works.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
169

## Slide 170
TOPIC 05 · HANDS-ON
Configure Extended ACLs to Mitigate Attacks
LAB 28
Configure and verify infrastructure security features — ACLs (ENCOR 5.2.a).
The security team wants the branch to permit only what the business needs and to block the traffic patterns behind the last incident: spoofed private source addresses arriving from the internet and unsolicited inbound ICMP. As the engineer you write named extended ACLs, place them correctly, and confirm the implicit deny is not silently dropping something you needed.
YOU'LL BUILD
Named extended ACLs permitting only required services, blocking spoofed RFC 1918 sources inbound and unsolicited ICMP, applied in the correct direction with verified hit counters.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1/R2/R3 routers, PC-A, PC-C, servers
DONE WHEN
'show access-lists INTERNET-IN' shows the entries in the intended order with match counters incrementing on the permit lines, spoofed private-source traffic is denied, permitted HTTP/HTTPS still reaches the server, and the logged deny shows what the implicit deny would have dropped.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
170

## Slide 171
LAB 28 · PROCESS MAP
How Lab 28 Runs
1
Open lab-28-acls/lab-28-acls.pkt and confirm PC1 can currently reach every service on the server
C:\> ping 172.22.34.62
2
Create a named extended ACL for the inbound internet edge
R1(config)# ip access-list extended INTERNET-IN
3
Block spoofed RFC 1918 sources arriving from outside
R1(config-ext-nacl)# deny ip 10.0.0.0 0.255.255.255 any
4
Block the 172.16.0.0/12 private range as a spoofed source
R1(config-ext-nacl)# deny ip 172.16.0.0 0.15.255.255 any
5
Block the 192.168.0.0/16 private range as a spoofed source
R1(config-ext-nacl)# deny ip 192.168.0.0 0.0.255.255 any
THE POINT
Configure and verify infrastructure security features — ACLs (ENCOR 5.2.a).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
171

## Slide 172
LAB 28 · VERIFY
Configure Extended ACLs to Mitigate Attacks
✅ Expected result
'show access-lists INTERNET-IN' shows the entries in the intended order with match counters incrementing on the permit lines, spoofed private-source traffic is denied, permitted HTTP/HTTPS still reaches the server, and the logged deny shows what the implicit deny would have dropped.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
172

## Slide 173
TOPIC 05 · HANDS-ON
Configure Control Plane Policing
LAB 29
Configure and verify infrastructure security features — CoPP (ENCOR 5.2.b).
During the last incident a flood of ICMP and SNMP drove the router CPU to 99% and OSPF adjacencies dropped — the device stopped routing because it was too busy answering management traffic. As the engineer you build a CoPP policy that rate-limits management and ICMP traffic to the control plane while guaranteeing routing protocol traffic always gets through.
YOU'LL BUILD
A CoPP policy applied to the control plane with separate classes for routing, management and ICMP, each policed at an appropriate rate, with verified conform and exceed counters.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1/R2 routers
DONE WHEN
'show policy-map control-plane' shows the three classes with conformed bytes on all of them and exceeded/dropped bytes on the ICMP class during the flood, while 'show ip ospf neighbor' confirms the adjacency never dropped.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
173

## Slide 174
LAB 29 · PROCESS MAP
How Lab 29 Runs
1
Open lab-29-copp/lab-29-copp.pkt and baseline the CPU utilisation
R1# show processes cpu sorted | include CPU
2
Create an ACL matching routing protocol traffic that must never be dropped
R1(config)# access-list 120 permit ospf any any
3
Add EIGRP and BGP to the same critical ACL
R1(config)# access-list 120 permit tcp any any eq 179
4
Create an ACL matching management traffic
R1(config)# access-list 121 permit tcp any any eq 22
5
Add SNMP to the management ACL
R1(config)# access-list 121 permit udp any any eq 161
THE POINT
Configure and verify infrastructure security features — CoPP (ENCOR 5.2.b).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
174

## Slide 175
LAB 29 · VERIFY
Configure Control Plane Policing
✅ Expected result
'show policy-map control-plane' shows the three classes with conformed bytes on all of them and exceeded/dropped bytes on the ICMP class during the flood, while 'show ip ospf neighbor' confirms the adjacency never dropped.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
175

## Slide 176
TOPIC 05 · HANDS-ON
Analyse Wireless Security, REST API Security and Security Design
LAB 30
Describe REST API security, configure wireless security features, and describe the components of network security design (ENCOR 5.3, 5.4, 5.5).
You are reviewing three security designs before sign-off: the wireless authentication model for a new floor, the API integration a vendor has proposed, and the overall segmentation design. As the engineer you evaluate each against the exam's criteria — walking the 802.1X and 4-way handshake exchanges, finding the flaws in the vendor's API design, and placing each defence layer.
YOU'LL BUILD
A completed wireless authentication comparison, an annotated 4-way handshake walkthrough, a REST API security review naming every flaw in the vendor proposal, and a layered security design map.
TOOLCHAIN
Cisco Packet Tracer, WLC GUI, Postman or curl, security review worksheets
DONE WHEN
Your wireless comparison recommends 802.1X for corporate, PSK or WebAuth for guest and MAB with profiling for headless devices; your 4-way handshake walkthrough has all four messages in order; and api-security-review.csv names the HTTP transport, the embedded credentials and the absent rate limiting as flaws with concrete fixes.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
176

## Slide 177
LAB 30 · PROCESS MAP
How Lab 30 Runs
1
Open lab-30-security-design/ and read the three review packs provided
2
Compare the wireless authentication methods in wireless-security.csv — PSK, 802.1X, WebAuth and MAB
3
Identify the three 802.1X roles: supplicant, authenticator and authentication server
4
Note that EAPOL carries EAP between supplicant and authenticator, and RADIUS carries it onward
5
Walk the 4-way handshake: the AP sends ANonce, the client replies with SNonce and a MIC
THE POINT
Describe REST API security, configure wireless security features, and describe the components of network security design (ENCOR 5.3, 5.4, 5.5).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
177

## Slide 178
LAB 30 · VERIFY
Analyse Wireless Security, REST API Security and Security Design
✅ Expected result
Your wireless comparison recommends 802.1X for corporate, PSK or WebAuth for guest and MAB with profiling for headless devices; your 4-way handshake walkthrough has all four messages in order; and api-security-review.csv names the HTTP transport, the embedded credentials and the absent rate limiting as flaws with concrete fixes.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
178

## Slide 179
TOPIC RECAP
Recap — Network Security
• You can now: Configure and verify device access control — lines and local user authentication (ENCOR 5.1.a).
• You can now: Configure and verify device access control — authentication and authorization using AAA (ENCOR 5.1.b).
• You can now: Configure and verify infrastructure security features — ACLs (ENCOR 5.2.a).
• You can now: Configure and verify infrastructure security features — CoPP (ENCOR 5.2.b).
• You can now: Describe REST API security, configure wireless security features, and describe the components of network security design (ENCOR 5.3, 5.4, 5.5).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
179

## Slide 180
TOPIC 06
Network Automation
Python · JSON · YANG · DNA Center and vManage APIs · REST responses · EEM · orchestration tools
06
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
180

## Slide 181
TOPIC 06 · SCOPE
Topic 06 — What This Domain Covers
1
Exam domain
ENCOR domain 6.0 Automation
2
Exam weighting
15% of the ENCOR 350-401 exam
3
TSC mapping
Skills Framework K6, A5 · Network Configuration (ICT-DIT-3009-1.1)
4
Hands-on labs
Labs 31–35 — every objective has a lab
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
181

## Slide 182
TOPIC WEIGHTING 15%
Key Concepts — Network Automation
1
The ENCOR exam asks you to interpret Python, not to write an application: you must read a script and predict its output, so lists, dictionaries, loops, conditionals, functions and the requests library are the working set.
2
A Python dictionary maps keys to values and is exactly how a parsed JSON object arrives — nested API responses are therefore navigated with chained keys and indexes such as response['response'][0]['hostname'].
3
JSON has six value types — string, number, boolean, null, array and object — with keys always in double quotes, no trailing commas and no comments; a single trailing comma is the most common invalid-JSON exam trap.
4
YANG is a data modelling language that defines the structure, types and constraints of configuration and operational data; NETCONF and RESTCONF are the protocols that carry data conforming to those models.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
182

## Slide 183
TOPIC WEIGHTING 15%
Key Concepts — Network Automation (2)
1
A YANG model is a tree of containers, lists, leaves and leaf-lists — a container groups, a list has a key and repeats, a leaf holds one typed value — and the same model drives both NETCONF XML and RESTCONF JSON.
2
The Cisco DNA Center Intent API is token-based: POST to /dna/system/api/v1/auth/token with Basic auth to receive an X-Auth-Token, then send that token in the header of every subsequent call.
3
The vManage API authenticates with a session cookie from /j_security_check plus an XSRF token for write operations, and exposes device inventory, statistics and policy over /dataservice endpoints.
4
REST response codes group by class: 2xx succeeded (200 OK, 201 Created, 204 No Content), 4xx you made an error (400 bad request, 401 unauthenticated, 403 unauthorised, 404 not found, 429 rate-limited), and 5xx the server failed.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
183

## Slide 184
TOPIC WEIGHTING 15%
Key Concepts — Network Automation (3)
1
A 401 means the token is missing, wrong or expired, while a 403 means the token is valid but the account lacks permission — reading that difference correctly is the fastest way to fix a failing API script.
2
EEM (Embedded Event Manager) runs on the device itself: an event detector (syslog, SNMP, interface, timer, CLI) triggers an applet whose actions run CLI commands, write logs, send mail or set variables — automation with no external server.
3
An EEM applet needs 'event manager applet NAME', one event statement, and numbered action statements which run in lexical order — so 1.0, 2.0, 3.0 is the safe numbering convention, not 1, 2, 10.
4
Agent-based tools (Puppet, Chef) install software on the managed node and pull the desired state on a schedule; agentless tools (Ansible, SaltStack in agentless mode) push over SSH or an API and are far easier to adopt on network devices that cannot run an agent.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
184

## Slide 185
TOPIC WEIGHTING 15%
Key Concepts — Network Automation (4)
1
Ansible is declarative and idempotent: a playbook describes the desired end state, and running it twice makes no second change — which is what makes it safe to re-run against production.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
185

## Slide 186
WHAT YOU'LL DO
Hands-On Labs — Network Automation
Labs 31–32
• Interpret Python Components and Scripts
• Construct and Validate JSON-Encoded Files
Labs 33–34
• Explore YANG Models and Call the DNA Center API
• Construct an EEM Applet to Automate Response
Lab 35
• Compare Agent and Agentless Orchestration Tools
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
186

## Slide 187
TOPIC 06 · HANDS-ON
Interpret Python Components and Scripts
LAB 31
Interpret basic Python components and scripts (ENCOR 6.1).
The ENCOR exam does not ask you to write an application — it shows you a script and asks what it prints. As the network engineer moving into automation, you work through the Python that actually appears in network scripts: lists and dictionaries holding device inventories, loops that iterate them, conditionals that branch on state, and functions that return values.
YOU'LL BUILD
A set of correctly predicted script outputs, a working device-inventory script that loops a list of dictionaries, and a written explanation of the one deliberate bug you fix.
TOOLCHAIN
Python 3.10+, VS Code or any editor, devices.py sample scripts
DONE WHEN
Your written predictions match the actual output of every script, inventory_report.py runs without error and prints one line per device, and buggy.py runs correctly after your fix with a comment explaining the indentation error.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
187

## Slide 188
LAB 31 · PROCESS MAP
How Lab 31 Runs
1
Open lab-31-python/ and read devices.py before running anything
2
Predict the output of the first script on paper, then run it and compare
python3 predict_01.py
3
Examine the list of device dictionaries that models the inventory
4
Access a single value by its key and print it
python3 -c "d={'host':'R1','ip':'10.1.1.1'}; print(d['ip'])"
5
Loop the inventory and print each device's hostname and IP
python3 loop_inventory.py
THE POINT
Interpret basic Python components and scripts (ENCOR 6.1).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
188

## Slide 189
LAB 31 · VERIFY
Interpret Python Components and Scripts
✅ Expected result
Your written predictions match the actual output of every script, inventory_report.py runs without error and prints one line per device, and buggy.py runs correctly after your fix with a comment explaining the indentation error.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
189

## Slide 190
TOPIC 06 · HANDS-ON
Construct and Validate JSON-Encoded Files
LAB 32
Construct valid JSON-encoded files (ENCOR 6.2).
Every REST API you will touch speaks JSON, and the exam presents you with JSON that is subtly invalid and asks you to spot why. As the automation engineer you construct a valid device inventory in JSON, deliberately break it in each of the classic ways, and learn to read a parser error back to the exact character that caused it.
YOU'LL BUILD
A valid nested JSON device inventory that passes validation, a set of four broken variants each demonstrating a different classic error, and a Python script that parses the valid file into a dictionary.
TOOLCHAIN
Python 3.10+, a text editor, json module, sample API payloads
DONE WHEN
devices.json validates cleanly with 'python3 -m json.tool', all four broken variants fail with a parser error you can explain, and your navigation command prints the correct nested interface name.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
190

## Slide 191
LAB 32 · PROCESS MAP
How Lab 32 Runs
1
Open lab-32-json/ and review the six JSON value types — string, number, boolean, null, array, object
2
Write a JSON object describing one device with hostname, IP, uptime and an enabled flag
3
Extend it into an array of three device objects
4
Nest an interfaces array inside each device to make the structure realistic
5
Validate the file with Python's json module
python3 -m json.tool devices.json
THE POINT
Construct valid JSON-encoded files (ENCOR 6.2).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
191

## Slide 192
LAB 32 · VERIFY
Construct and Validate JSON-Encoded Files
✅ Expected result
devices.json validates cleanly with 'python3 -m json.tool', all four broken variants fail with a parser error you can explain, and your navigation command prints the correct nested interface name.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
192

## Slide 193
TOPIC 06 · HANDS-ON
Explore YANG Models and Call the DNA Center API
LAB 33
Describe the principles and benefits of YANG, describe APIs for Cisco DNA Center and vManage, and interpret REST API response codes (ENCOR 6.3, 6.4, 6.5).
Your team is scripting against Cisco DNA Center, and the first attempts are failing with codes nobody can interpret. As the automation engineer you walk the YANG model that defines the data, authenticate correctly to obtain an X-Auth-Token, then work through the response codes deliberately — including the 401 versus 403 distinction that decides whether you fix the token or the account's permissions.
YOU'LL BUILD
A YANG model walkthrough naming containers, lists and leaves, a successful token request, a device inventory retrieved with that token, and a completed response-code interpretation table.
TOOLCHAIN
Python 3.10+, requests library, curl or Postman, DNA Center sandbox or provided mock API
DONE WHEN
The token request returns 200 with a Token value, the authenticated inventory call returns 200 with a device list, the unauthenticated call returns 401, and response-codes.csv correctly distinguishes 401 (fix the token) from 403 (fix the permissions).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
193

## Slide 194
LAB 33 · PROCESS MAP
How Lab 33 Runs
1
Open lab-33-yang-dnac/ and read the ietf-interfaces YANG model extract provided
2
Identify the container — the node that groups related data but does not repeat
3
Identify the list and its key — the node that repeats, one entry per interface
4
Identify the leaves and their types — name is a string, enabled is a boolean
5
State the benefit: one model drives both NETCONF XML and RESTCONF JSON
THE POINT
Describe the principles and benefits of YANG, describe APIs for Cisco DNA Center and vManage, and interpret REST API response codes (ENCOR 6.3, 6.4, 6.5).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
194

## Slide 195
LAB 33 · VERIFY
Explore YANG Models and Call the DNA Center API
✅ Expected result
The token request returns 200 with a Token value, the authenticated inventory call returns 200 with a device list, the unauthenticated call returns 401, and response-codes.csv correctly distinguishes 401 (fix the token) from 403 (fix the permissions).
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
195

## Slide 196
TOPIC 06 · HANDS-ON
Construct an EEM Applet to Automate Response
LAB 34
Construct an EEM applet to automate configuration, troubleshooting or data collection (ENCOR 6.6).
A critical WAN interface flaps at night and nobody captures the state before it recovers, so the cause is never found. As the engineer you make the device investigate itself: an EEM applet that triggers on the syslog message, runs the diagnostic commands, writes the output to a file and logs a summary — automation with no external server involved.
YOU'LL BUILD
Two working EEM applets — one syslog-triggered applet that collects diagnostics on an interface down event, and one timed applet that logs a periodic health snapshot.
TOOLCHAIN
Cisco Packet Tracer, Cisco IOS CLI, R1 router
DONE WHEN
'show event manager policy registered' lists both applets, shutting Serial0/0/0 produces the 'EEM: Serial0/0/0 down' syslog entry, and 'show event manager statistics policy' shows a non-zero run count for the triggered applet.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
196

## Slide 197
LAB 34 · PROCESS MAP
How Lab 34 Runs
1
Open lab-34-eem/lab-34-eem.pkt and confirm you can see the interface down syslog message
R1# show logging | include LINEPROTO
2
Create the applet and give it a descriptive name
R1(config)# event manager applet INTERFACE-DOWN
3
Define the syslog event detector matching the interface down pattern
R1(config-applet)# event syslog pattern "Interface Serial0/0/0, changed state to down"
4
Add the first action — enter privileged mode, since the applet starts unprivileged
R1(config-applet)# action 1.0 cli command "enable"
5
Collect the interface state
R1(config-applet)# action 2.0 cli command "show interfaces Serial0/0/0"
THE POINT
Construct an EEM applet to automate configuration, troubleshooting or data collection (ENCOR 6.6).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
197

## Slide 198
LAB 34 · VERIFY
Construct an EEM Applet to Automate Response
✅ Expected result
'show event manager policy registered' lists both applets, shutting Serial0/0/0 produces the 'EEM: Serial0/0/0 down' syslog entry, and 'show event manager statistics policy' shows a non-zero run count for the triggered applet.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
198

## Slide 199
TOPIC 06 · HANDS-ON
Compare Agent and Agentless Orchestration Tools
LAB 35
Compare agent versus agentless orchestration tools such as Chef, Puppet, Ansible and SaltStack (ENCOR 6.7).
Your organisation must pick one configuration management tool for a network of 300 Cisco devices that cannot run third-party agents. As the engineer making the recommendation you compare the four tools on architecture, transport, language and network-device suitability, then write and read a small Ansible playbook to prove the agentless model works on IOS.
YOU'LL BUILD
A completed four-tool comparison matrix, a written recommendation justified on the agent constraint, and an annotated Ansible playbook that configures an IOS interface idempotently.
TOOLCHAIN
Python 3.10+, Ansible, a text editor, tool comparison worksheet
DONE WHEN
orchestration-comparison.csv correctly classifies Puppet and Chef as agent-based pull and Ansible as agentless push, the playbook reports changed=1 on the first run and changed=0 on the second, and your recommendation names Ansible with the no-agent constraint as the reason.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
199

## Slide 200
LAB 35 · PROCESS MAP
How Lab 35 Runs
1
Open lab-35-orchestration/ and read the requirement: 300 IOS devices, no agents permitted
2
Record Puppet's architecture — agent-based, pull model, Ruby DSL, master/agent
3
Record Chef's architecture — agent-based, pull model, Ruby recipes and cookbooks
4
Record Ansible's architecture — agentless, push model, YAML playbooks over SSH or API
5
Record SaltStack's architecture — minion-based by default, but supports agentless SSH mode
THE POINT
Compare agent versus agentless orchestration tools such as Chef, Puppet, Ansible and SaltStack (ENCOR 6.7).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
200

## Slide 201
LAB 35 · VERIFY
Compare Agent and Agentless Orchestration Tools
✅ Expected result
orchestration-comparison.csv correctly classifies Puppet and Chef as agent-based pull and Ansible as agentless push, the playbook reports changed=1 on the first run and changed=0 on the second, and your recommendation names Ansible with the no-agent constraint as the reason.
IF IT DOESN'T WORK
Nothing happens
Check the .env file is in the labs folder and the key has no quotes or spaces.
Auth or 401 error
Re-copy the API key from AI Studio; confirm GOOGLE_GENAI_USE_VERTEXAI=0.
ModuleNotFoundError
Run uv sync again, and prefix commands with uv run so the venv is used.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
201

## Slide 202
TOPIC RECAP
Recap — Network Automation
• You can now: Interpret basic Python components and scripts (ENCOR 6.1).
• You can now: Construct valid JSON-encoded files (ENCOR 6.2).
• You can now: Describe the principles and benefits of YANG, describe APIs for Cisco DNA Center and vManage, and interpret REST API response codes (ENCOR 6.3, 6.4, 6.5).
• You can now: Construct an EEM applet to automate configuration, troubleshooting or data collection (ENCOR 6.6).
• You can now: Compare agent versus agentless orchestration tools such as Chef, Puppet, Ansible and SaltStack (ENCOR 6.7).
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
202

## Slide 203
WRAP-UP
Course Summary & Next Steps
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
203

## Slide 204
LEARNING OUTCOMES
What You Achieved
1
LO1 · Translated requirements
Turned organisational needs into campus, wireless and WAN designs — 2-tier versus 3-tier, deployment models and QoS policy.
2
LO2 · Selected components
Chose and configured the right components: VRFs, tunnels, switches, routers, controllers and their interdependencies.
3
LO3 · Implemented devices
Configured trunking, EtherChannel, RSTP, MST, EIGRP, OSPFv2/v3, eBGP, NAT, HSRP and controller-based wireless.
4
LO4 · Managed access
Secured device access with SSH and AAA, enforced ACLs and CoPP, and deployed 802.1X and WPA2-Enterprise wireless.
5
LO5 · Deployed tools
Deployed syslog, SNMPv3, Flexible NetFlow, SPAN/RSPAN, IP SLA, NETCONF and RESTCONF.
6
LO6 · Reported and assessed
Automated reporting and response with Python, JSON, REST APIs, EEM applets and Ansible.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
204

## Slide 205
NEXT STEPS
Your Path to CCNP Enterprise
1
1 · Pass ENCOR 350-401
The core exam you have prepared for this week. Passing it alone earns Cisco Certified Specialist – Enterprise Core.
2
2 · Choose a concentration
CCNP Enterprise = ENCOR plus one concentration exam. ENARSI (advanced routing) is the most common next step.
3
3 · Practise the pacing
Use the practice exam at exams.tertiaryinfotech.com in Exam mode until 100 questions in 120 minutes feels comfortable.
4
4 · Rebuild every lab
Redo each of the 35 labs from a blank configuration until the commands come without the guide.
5
5 · Read the blueprint again
Walk learningnetwork.cisco.com/s/encor-exam-topics objective by objective and rate your confidence on each.
6
6 · Book the exam
Schedule at a Pearson VUE centre once you are consistently scoring above 85% in Exam mode.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
205

## Slide 206
PRACTICE EXAM · exams.tertiaryinfotech.com
Practice Exam — Book Your Revision Now
1
Where
exams.tertiaryinfotech.com/practice-exams/cisco/cisco-ccnp-encor
2
What
200 original questions across two full 100-question practice exams.
3
How long
120 minutes each — the same as the real 350-401 exam.
4
Practice mode
Immediate answers and explanations. Use it while the material is still fresh.
5
Exam mode
Timed with answers hidden until submission. Use it in your final week.
6
Free sample
A free sample exam is available with no payment details required.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
206

## Slide 207
CONTINUE WITH TERTIARY INFOTECH
Recommended Courses
1
WSQ Cisco Certified Network Associate (CCNA) Training
2
WSQ Cisco Certified Network Professional (CCNP) for ENARSI Training
3
WSQ Certified Ethical Hacker (CEH) Training
4
WSQ ISC2 Certified Information Systems Security Professional (CISSP) Training
5
WSQ CompTIA Network+ Training
6
WSQ Network Automation with Python and Ansible
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
207

## Slide 208
WE'RE HERE TO HELP
Support
• If you have any enquiries during or after the class, you can contact us below.
• Email: enquiry@tertiaryinfotech.com
• Tel: +65 6100 0613
• Website: www.tertiarycourses.com.sg
• LMS / TMS: https://lms-tms.tertiaryinfotech.com
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
208

## Slide 209
WRAP-UP
Final Assessment
1
Written Assessment (SAQ)
1 hour · open book · short-answer knowledge questions across all six domains.
2
Practical Performance (PP)
1 hour · open book · hands-on Cisco configuration and verification tasks.
3
Digital attendance
Remember to take the Assessment digital attendance (TRAQOM) before you start.
4
Submit on the LMS
Upload your completed answers at https://lms-tms.tertiaryinfotech.com/
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
209

## Slide 210
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey
Scan the QR code on the LMS
2
Digital attendance
Scan the SSG assessment QR
3
Sit WA then PP
Open book · 1 hour each
4
Submit on the LMS
Upload your completed answers
5
Sign the record
Sign the Assessment Summary Record
REMEMBER
All five steps are mandatory for WSQ funding — missing the digital attendance or the TRAQOM survey can invalidate your claim.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
210

## Slide 211
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
1
Three times a day
Take the AM, PM and Assessment digital attendance — mandatory for every WSQ-funded course.
2
Trainer shows the QR
The trainer or administrator displays the digital attendance QR code from the SSG portal.
3
Scan and submit
Scan the QR code with your mobile phone camera and submit your attendance.
4
75% minimum
A minimum of 75% attendance is required to be eligible for assessment and funding.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
211

## Slide 212
GOOD LUCK IN THE EXAM
Thank You!
You can now design, implement, secure and automate the core technologies of a Cisco enterprise network — and you are ready to sit ENCOR 350-401.
Cisco Certified Network Professional (CCNP) for ENCOR Training · TGS-2024044052
© 2026 Tertiary Infotech Academy Pte Ltd
212